## Slide 1: CS2100 Tutorial #2
Song Kai
song.kai@u.nus.edu

## Slide 2: Q1 Bitwise Operations
byte_t a, b;
a = 5;
b = 22;
printf("a = "); printByte(a); printf("\n");
printf("b = "); printByte(b); printf("\n");
a = 00000101
b = 00010110
8 bit

## Slide 3: Q1 Bitwise Operations
a = 00000101
b = 00010110
a|b = ?
a&b = ?
a^b = ?
~a = ?
a << 2 = ?
b >> 3 = ?
| (bitwise OR)
& (bitwise AND)
^ (bitwise XOR)
~ (1’s complement)
<< (left shift)
>> (right shift)

## Slide 4: Q1 Bitwise Operations – Bitwise OR
byte_t a, b;
a = 5;
b = 22;
printf("a|b = "); printByte(a|b); printf("\n");
8 bit
a = 00000101
b = 00010110
----------
a|b = 00010111
x | y | x OR y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Recall:
  x OR 0 = x
  x OR 1 = 1
Notes: OR can be used to set certain bits to 1 while keeping the rest unchanged

## Slide 5: Q1 Bitwise Operations – Bitwise AND
byte_t a, b;
a = 5;
b = 22;
printf("a&b = "); printByte(a&b); printf("\n");
8 bit
a = 00000101
b = 00010110
----------
a&b = 00000100
x | y | x AND y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Recall:
  x AND 0 = 0
  x AND 1 = x
Notes: AND can be used as a mask to keep only the bits we want

## Slide 6: Q1 Bitwise Operations – Bitwise XOR
byte_t a, b;
a = 5;
b = 22;
printf("a^b = "); printByte(a^b); printf("\n");
8 bit
a = 00000101
b = 00010110
----------
a^b = 00010011
x | y | x XOR y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Recall:
  x XOR 0 = x
  x XOR 1 = x'
Notes: XOR is to check: are the two bits different?
XOR can be used to negate bits

## Slide 7: Q1 Bitwise Operations – 1s Complement
byte_t a, b;
a = 5;
b = 22;
printf(“~a = "); printByte(~a); printf("\n");
8 bit
a = 00000101
~a = 11111010
Notes: Negation, or the NOT operator

## Slide 8: Q1 Bitwise Operations – Left Shift
byte_t a, b;
a = 5;
b = 22;
printf("a << 2 = "); printByte(a << 2); printf("\n");
8 bit
a = 00000101
a << 2 = 00010100
Equivalent to a *= 4
But faster!
Notes: A shifting operations are more efficient than multiplication and division. It is a basic operation supported by the processor. Shift operations typically execute in constant time, meaning they take the same amount of time regardless of the size of the shift. Multiplication and division can require more complex operations that take longer to compute, especially for large numbers.

## Slide 9: Q1 Bitwise Operations – Right Shift
byte_t a, b;
a = 5;
b = 22;
printf(“b >> 3 = "); printByte(b >> 3); printf("\n");
8 bit
b = 00010110
b >> 3 = 00000010
Equivalent to b /= 8
Notes: Whole division since we discard the bits shifted out

## Slide 10
Q1.
What is ? :
Conditional operator
condition ? true-part : false-part
If the condition is true, it returns the true-part value; otherwise, it returns the false-part value.
Example:
int a, b, c;
…
c = (a>b ? a+100 : b-10);
If a=12, b=34, then c becomes …
If a=34, b=12, then c becomes …
24
134

## Slide 11: Backup – Q1
x & 1000 0000
x & 0100 0000
x & 0010 0000
x & 0001 0000
x & 0000 1000
x & 0000 0100
x & 0000 0010
x & 0000 0001
Get value from MSB to LSB one by one.

## Slide 12
Operation | Opcode in MIPS | Immediate Version (if applicable)
Addition | add $s0, $s1, $s2 | addi $s0, $s1, C162s
Subtraction | sub $s0, $s1, $s2 | 
Shift left logical | sll $s0, $s1, C5 | 
Shift right logical | srl $s0, $s1, C5 | 
AND bitwise | and $s0, $s1, $s2 | andi $s0, $s1, C16
OR bitwise | or $s0, $s1, $s2 | ori $s0, $s1, C16
NOR bitwise | nor $s0, $s1, $s2 | 
XOR bitwise | xor $s0, $s1, $s2 | xori $s0, $s1, C16
Load Upper Immediate |  | lui $s0, C16
MIPS Basic Instructions Checklist (1)
$s0 is the destination
C5 is [0 to 25-1]
C162s is [-215 to 215-1]
C16 is a 16-bit pattern
Notes: NOT = NOR 0
LUI + ORI = load 32 bit

## Slide 13
Q2.
(a) Set bits 2, 8, 9, 14 and 16 of b to 1. Leave the other bits unchanged.
Example: Before
b = 0011 0000 0111 0000 0110 1101 0010 0001.
(Bits 2, 8, 9, 14 and 16 are underlined.)
lui $t0, 0b1 # set bit 16.
ori $t0, $t0, 0b0100 0011 0000 0100 # set bits 14,9,8,2.
or $s1, $s1, $t0
Recall:
  x OR 0 = x
  x OR 1 = 1
Variable mapping: a  $s0; b  $s1; c  $s2
After
b = 0011 0000 0111 0001 0110 1111 0010 0101.
ori $s1, $s1, 0b0000 0000 0000 0001 0100 0011 0000 0100
Conceptually:

## Slide 14
Q2.
(b) Copy over bits 1, 3 and 7 of b into a, without changing any other bits of a.
Example: Before (assume that the most significant 24 bits are all zeroes)
a = 0 0 … 0 0 0 0 1 0 1 0 1 0.
b = 0 0 … 0 0 1 1 0 1 1 1 0 0.
After
a = 0 0 … 0 0 1 0 1 0 1 0 0 0.
b = 0 0 … 0 0 1 1 0 1 1 1 0 0.
andi $t0, $s1, 0b0000 0000 1000 1010
lui $t1, 0b1111 1111 1111 1111
ori $t1, $t1, 0b1111 1111 0111 0101
and $s0, $s0, $t1
or $s0, $s0, $t0
Recall:
  x AND 0 = 0
  x AND 1 = x
Recall:
  x OR 0 = x
  x OR 1 = 1
Variable mapping: a  $s0; b  $s1; c  $s2
Get bits 1, 3 and 7 of b
Get the rest of bits of a
  Use a 32-bit mask
Combine them together

## Slide 15
Q2.
(c) Make bits 2, 4 and 8 of c the inverse of bits 1, 3 and 7 of b.
Example: Before (assume that the … part are all zeroes)
b = 0 0 … 0 0 1 1 0 1 1 1 0 0.
c = 0 0 … 0 1 0 0 1 0 1 0 1 0.
After
b = 0 0 … 0 0 1 1 0 1 1 1 0 0.
c = 0 0 … 0 0 0 0 1 0 1 1 1 0.
Recall:
  x XOR 0 = x
  x XOR 1 = x'
xori $t0, $s1, 0b1000 1010
andi $t0, $t0, 0b1000 1010
sll $t0, $t0, 1
lui $t1, 0b1111 1111 1111 1111
ori $t1, $t1, 0b1111 1110 1110 1011
and $s2, $s2, $t1
or $s2, $s2, $t0
Variable mapping: a  $s0; b  $s1; c  $s2
Prepare b
  Negate bits 1, 3 and 7 of b
  Set other bits to 0
  Left shift by 1 position to bits 2, 4 and 8
Prepare c
  Get all bits of c except bits 2, 4 and 8
    Use a 32-bit mask
Combine them together
Notes: Negation  XOR
We cannot revert the sequence of 1.1 and 1.2, or the zero bits will be inverted to 1

## Slide 16
Q3.
(a) c = a + b
Variable mapping: a  $s0; b  $s1; c  $s2; d  $s3
add $s2, $s0, $s1

## Slide 17
Q3.
(b) d = a + b - c
Variable mapping: a  $s0; b  $s1; c  $s2; d  $s3
d = a + b
d = d - c
add $s3, $s0, $s1
sub $s3, $s3, $s2
d = a – c
d = d + b
d = b – c
d = d + a
Alternatives:

## Slide 18
Q3.
(c) c = 2b + (a – 2)
c = b * 2
t0 = a – 2
c = c + t0
sll $s2, $s1, 1
addi $t0, $s0, -2
add $s2, $s2, $t0
Alternatives:
c = b + b

## Slide 19
Q3.
(d) d = 6a + 3(b – 2c)
t0 = 4a + 2a
2 sll and 1 add
t1 = b – 2c
1 sll and 1 sub
t2 = 2t1 + t1
1 sll and 1 add
d = t0 + t2
1 add
8 instructions
d = 3(2a + b – 2c)
t0 = 2a + b
1 sll and 1 add
t0 = t0 – 2c
1 sll and 1 sub
d = 2t0 + t0
1 sll and 1 add
6 instructions
d = 3(2(a - c) + b)
t0 = 2(a - c)
1 sub and 1 sll
t0 = t0 + b
1 add
d = 2t0 + t0
1 sll and 1 add
5 instructions
sub $t0, $s0, $s2 # t0 = a – c
sll $t0, $t0, 1 # t0 = 2(a – c)
add $t0, $t0, $s1 # t0 = 2(a – c) + b
sll $t1, $t0, 1 # t1 = 2(2(a – c) + b)
add $s3, $t1, $t0 # d = 3(2(a – c) + b)
Notes: Powers of 2 are easy, getting other multiplier is difficult.

## Slide 20
Q4.
$s0 is a 31-bit binary sequence with MSB=0.
add $t0, $s0, $zero
lui $t1, 0x8000
lp: beq $t0, $zero, e
andi $t2, $t0, 1
beq $t2, $zero, s
xor $s0, $s0, $t1
s: srl $t0, $t0, 1
j lp
e:
$s0 =
0 0 … 0 0 0 1 1 1 1 1
MSB
$t0 =
0 0 … 0 0 0 1 1 1 1 1
$t1 =
1000 0000 0000 0000 0000 0000 0000 0000
$t2 =
0 0 … 0 0 0 0 0 0 0 1
andi extracts the LSB of $t0 into $t2
xor toggles the MSB of $s0
1
0 0 … 0 0 0 0 1 1 1 1
Example: $s0 = 31
Q: At most how many iterations?
31
Q: What happens in each iteration?
Toggle the MSB of $s0 if $t2 = 1.
Q: What is the final value of $s0 (in hexadecimal)?
MSB of $s0 toggled for 5 times
0x8000 001F

## Slide 21
Q4.
$s0 is a 31-bit binary sequence with MSB=0.
add $t0, $s0, $zero
lui $t1, 0x8000
lp: beq $t0, $zero, e
andi $t2, $t0, 1
beq $t2, $zero, s
xor $s0, $s0, $t1
s: srl $t0, $t0, 1
j lp
e:
$s0 =
0 000 1010 1010 1010 1010 1010 1010 1010
MSB
$t0 =
$t1 =
1000 0000 0000 0000 0000 0000 0000 0000
Example:
$s0 = 0x0AAAAAAA
0 000 1010 1010 1010 1010 1010 1010 1010
Q: What is the final value of $s0 (in hexadecimal)?
Each A contains two 1 bits
MSB of $s0 is toggled for 14 times
0x0AAAAAAA

## Slide 22
Q4.
$s0 is a 31-bit binary sequence with MSB=0.
add $t0, $s0, $zero
lui $t1, 0x8000
lp: beq $t0, $zero, e
andi $t2, $t0, 1
beq $t2, $zero, s
xor $s0, $s0, $t1
s: srl $t0, $t0, 1
j lp
e:
$s0 = 31
$s0 = 0 0000000000000000000000000011111
MSB
After:
$s0 = 1 0000000000000000000000000011111
Before:
$s0 = 0x0AAAAAAA
$s0 = 0 0001010101010101010101010101010
Before:
After:
$s0 = 0 0001010101010101010101010101010
Summary
Odd number of 1’s in $s0: MSB  1
Even number of 1’s in $s0: MSB  0.
This is known as even parity bit scheme.
(Odd parity bit scheme defined similarly.)
Notes: The code sets bit 31 of $s0 to 1 if there are odd number of ‘1’ in $s0 initially, or 0 if there are even number of ‘1’. (This is called even parity bit scheme, where we want to ensure that $s0 have an even number of 1s)

## Slide 23
MIPS Basic Instructions Checklist (2)
Operation | Opcode in MIPS | Immediate Version (if applicable)
Load word | lw $s0, offset($s1) | 
Store word | sw $s0, offset($s1) | 
Branch on equal | beq $t0, $t1, label | 
Branch on not equal | bne $t0, $t1, label | 
Set on less than | slt $s0, $s1, $s2 | slti $s0, $s1, C162s
Jump | j label | 
$s0 is the destination
C162s is [-215 to 215-1]
offset is usually in multiples of 2n, usually 4
Notes: slt a < b  1, else 0
slt + beq = bge
slt + bne = blt

## Slide 24: Backup – Tut 1 Q1
Prove that the decimal value of an n-bit 2s complement can be calculated by negating the weight of the (n-1)th bit, i.e.
-(n - 1)th bit * 2n-1 + (n - 2)th bit * 2n-2 + (n - 3)th bit * 2n-3 + … + 1st bit * 20
For example, (11010001)2s = -128 + 64 + 16 + 1 = -47, (10110101)2s = -128 + 32 + 16 + 4 + 1 = -75
The claim is true for positive integers:
A positive number X always has its 2s complement X. The (n-1)th bit of X is 0 and does not affect the calculation.
Now consider a negative number -X, X > 0. -X has 2s complement (2n - X).
Let us look at (2n - X) in binary:
The (n-1)th bit of (2n - X) is 1, representing 2n-1
The other bits together must represent the remaining values: (2n - X) - 2n-1 = 2n-1 - X
If we negate the weight of (n-1)th of (2n - X), the equation above reduces to -X.
-(n - 1)th bit * 2n-1 + (n - 2)th bit * 2n-2 + (n - 3)th bit * 2n-3 + … + 1st bit * 20
= -2n-1 + 2n-1 - X
= -X
This proves the claim.

## Slide 25: Clarification on lui Instruction
lui $s0, C16
The instruction places the 16-bit immediate value in the upper half of the register, and at the same time, sets the lower 16 bits to zeros.
For example,
ori $t0, $zero, 0xFFFF // $t0 contains 0x0000FFFF
lui $t0, 0xF0F0 // $t0 contains 0xF0F00000
// 0xFFFF at lower 16 bits is cleared

## Slide 26: CS2100 Tutorial #2
Song Kai
song.kai@u.nus.edu