## Slide 1: CS2100 Tutorial 4
Song Kai
song.kai@u.nus.edu

## Slide 2: Addressing Mode
Methods to specify the location of a value as operand
Immediate addressing: give the value immediately.
  addi $t1, $t2, 10
Register addressing: value stored in a register
  add $t1, $t2, $t3
Displacement addressing: combine base and a displacement value to get address.
  lw $t1, 4($t2)
PC-relative addressing: calculate address relatively from PC value
  beq $t1, $2, label
Peudo-direct addressing: Obtain full target address from instruction and (PC+4)
  j target

## Slide 3: Qn 1 Instruction Formats
(a) op $t1, $t2
$s0 = 100 mem (100) = 1000
$s1 = 160 mem (160) = 1600
$s2 = 200 mem (200) = 2000
$s3 = 240 mem (240) = 2400
$s4 = 300 mem (300) = 3000
$t0 = 10000 mem (10000) = 100
$t1 = 15000 mem (15000) = 150
$t2 = 20000 mem (20000) = 200
$t3 = 25000 mem (25000) = 250
$t4 = 30000 mem (30000) = 300
Operand | Target Memory Address | Content
$t1 | NA | 15000
$t2 | NA | 20000
Notes: Register addressing: value stored in a register

## Slide 4: Qn 1 Instruction Formats
(b) op $s2, 100($zero)
$s0 = 100 mem (100) = 1000
$s1 = 160 mem (160) = 1600
$s2 = 200 mem (200) = 2000
$s3 = 240 mem (240) = 2400
$s4 = 300 mem (300) = 3000
$t0 = 10000 mem (10000) = 100
$t1 = 15000 mem (15000) = 150
$t2 = 20000 mem (20000) = 200
$t3 = 25000 mem (25000) = 250
$t4 = 30000 mem (30000) = 300
Operand | Target Memory Address | Content
$s2 | NA | 200
100($zero) | 100 | 1000
Notes: Displacement - combine base and a displacement value to get address.
Base – displacement mode
Base register – immediate displacement mode
If the value is an address, we go to the address and read the value

## Slide 5: Qn 1 Instruction Formats
(c) op $t4, 40($s2)
$s0 = 100 mem (100) = 1000
$s1 = 160 mem (160) = 1600
$s2 = 200 mem (200) = 2000
$s3 = 240 mem (240) = 2400
$s4 = 300 mem (300) = 3000
$t0 = 10000 mem (10000) = 100
$t1 = 15000 mem (15000) = 150
$t2 = 20000 mem (20000) = 200
$t3 = 25000 mem (25000) = 250
$t4 = 30000 mem (30000) = 300
Operand | Target Memory Address | Content
$t4 | NA | 30000
40($s2) | 240 | 2400

## Slide 6: Qn 1 Instruction Formats
(d) op $s3, 200($zero)
$s0 = 100 mem (100) = 1000
$s1 = 160 mem (160) = 1600
$s2 = 200 mem (200) = 2000
$s3 = 240 mem (240) = 2400
$s4 = 300 mem (300) = 3000
$t0 = 10000 mem (10000) = 100
$t1 = 15000 mem (15000) = 150
$t2 = 20000 mem (20000) = 200
$t3 = 25000 mem (25000) = 250
$t4 = 30000 mem (30000) = 300
Operand | Target Memory Address | Content
$s3 | NA | 240
200($zero) | 200 | 2000

## Slide 7: Qn 1 Instruction Formats
(e) op $t3, $zero($t1)
$s0 = 100 mem (100) = 1000
$s1 = 160 mem (160) = 1600
$s2 = 200 mem (200) = 2000
$s3 = 240 mem (240) = 2400
$s4 = 300 mem (300) = 3000
$t0 = 10000 mem (10000) = 100
$t1 = 15000 mem (15000) = 150
$t2 = 20000 mem (20000) = 200
$t3 = 25000 mem (25000) = 250
$t4 = 30000 mem (30000) = 300
Operand | Target Memory Address | Content
$t3 | NA | 25000
$zero($t1) | Illegal | Illegal
Notes: This is base register – displacement register mode (hypothetically)

## Slide 8: Qn 1 Instruction Formats
(f) op $s1, 140($s1)
$s0 = 100 mem (100) = 1000
$s1 = 160 mem (160) = 1600
$s2 = 200 mem (200) = 2000
$s3 = 240 mem (240) = 2400
$s4 = 300 mem (300) = 3000
$t0 = 10000 mem (10000) = 100
$t1 = 15000 mem (15000) = 150
$t2 = 20000 mem (20000) = 200
$t3 = 25000 mem (25000) = 250
$t4 = 30000 mem (30000) = 300
Operand | Target Memory Address | Content
$s1 | NA | 160
140($s1) | 300 | 3000

## Slide 9
3.1 Storage Architecture: Example
Stack | Accumulator | Register (load-store) | Memory-Memory
Push A | Load A | Load R1,A | Add C, A, B
Push B | Add B | Load R2,B | 
Add | Store C | Add R3,R1,R2 | 
Pop C |  | Store R3,C | 
C = A+B
Memory-Memory
Stack
Accumulator
Register-register/load-store

## Slide 10
20
10
3.1 Storage Architecture: Animation
Stack | Accumulator | Register (load-store) | Memory-Memory
Push A | Load A | Load R1,A | Add C, A, B
Push B | Add B | Load R2,B | 
Add | Store C | Add R3,R1,R2 | 
Pop C |  | Store R3,C | 
Push A
Push B
Add
Pop C
Stack
10
20
?
...
...
Memory
Variable Name
This is information remembered by the compiler.
A
B
...
...
30
30
C

## Slide 11
3.1 Storage Architecture: Animation
Stack | Accumulator | Register (load-store) | Memory-Memory
Push A | Load A | Load R1,A | Add C, A, B
Push B | Add B | Load R2,B | 
Add | Store C | Add R3,R1,R2 | 
Pop C |  | Store R3,C | 
Load A
Add B
Store C
?
Accumulator
10
20
?
...
...
Memory
Variable Name
This is information remembered by the compiler.
A
B
...
...
30
C
This is a special register!
10
30

## Slide 12
3.1 Storage Architecture: Animation
Stack | Accumulator | Register (load-store) | Memory-Memory
Push A | Load A | Load R1,A | Add C, A, B
Push B | Add B | Load R2,B | 
Add | Store C | Add R3,R1,R2 | 
Pop C |  | Store R3,C | 
Load R1,A
Load R2,B
Add R3,R1,R2
Store R3,C
Registers
10
20
?
...
...
Memory
Variable Name
This is information remembered by the compiler.
A
B
...
...
30
C
These are general purpose registers
...
...
?
?
?
10
20
30
R1
R2
...
...
R3
Notes: This is actually Register-Register

## Slide 13
3.1 Storage Architecture: Animation
Stack | Accumulator | Register-Memory | Memory-Memory
Push A | Load A | MOV R1,[A] | Add C, A, B
Push B | Add B | ADD R1,[B] | 
Add | Store C | MOV [C], R1 | 
Pop C |  |  | 
MOV R1, [A]
ADD R1, [B]
MOV [C], R1
Registers
10
20
?
...
...
Memory
Variable Name
This is information remembered by the compiler.
A
B
...
...
30
C
These are general purpose registers
...
...
?
10
R1
...
...
30
Notes: Register-Memory taking reference from X86
Move the value at the latter to the former
Instead of loading values from address into registers for further processing, we can directly perform calculations from the value at the address

## Slide 14
3.1 Storage Architecture: Animation
Stack | Accumulator | Register (load-store) | Memory-Memory
Push A | Load A | Load R1,A | Add C, A, B
Push B | Add B | Load R2,B | 
Add | Store C | Add R3,R1,R2 | 
Pop C |  | Store R3,C | 
Add C, A, B
10
20
?
...
...
Memory
Variable Name
This is information remembered by the compiler.
A
B
...
...
30
C

## Slide 15: Qn 2 Instruction Set Architectures
Stack
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
Older Value
Older Value
Older Value
Older Value
•
•
•
Top of stack
push @a1
push @a2
add
pop @a0

## Slide 16: Qn 2 Instruction Set Architectures
Stack
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
Older Value
Older Value
Older Value
Older Value
•
•
•
Top of stack
push @a0
push @a2
add
pop @a1

## Slide 17: Qn 2 Instruction Set Architectures
Stack
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
Older Value
Older Value
Older Value
Older Value
•
•
•
Top of stack
push @a0
push @a1
add
pop @a2

## Slide 18: Qn 2 Instruction Set Architectures
Accumulator
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
Accumulator
Old Value
load @a1
add @a2
store @a0

## Slide 19: Qn 2 Instruction Set Architectures
Accumulator
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
Accumulator
Value @a0
add @a2
store @a1
Notes: The optimization is not compulsory

## Slide 20: Qn 2 Instruction Set Architectures
Accumulator
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
Accumulator
Value @a1
add @a0
store @a2

## Slide 21: Qn 2 Instruction Set Architectures
Memory-Memroy
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
add @a0, @a1, @a2
add @a1, @a0, @a2
add @a2, @a0, @a1

## Slide 22: Qn 2 Instruction Set Architectures
Register-Register
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
load $r1, @a1
load $r2, @a2
add $r0, $r1, $r2
store $r0, @a0
add $r1, $r0, $r2
store $r1, @a1
add $r2, $r0, $r1
store $r2, @a2
a0  $r0
a1  $r1
a2  $r2

## Slide 23: Qn 3 Instruction Design
Constraints:
16-bit processor
3 bits opcode
128 bytes of byte-addressable memory
5 registers
Fixed-length instructions
7-bit address for 128 locations
3-bit register code for 5 registers
Instruction length should be multiples of 2 bytes
Notes: design a dedicated 16-bit processor: the processor handles data / instruction in 16 bits each time. It is ideal to have instructions to be in multiples of 16 bits to align data bus, memory and register operations
Fixed-length instructions means that all instructions should be as long as the longest instruction

## Slide 24: Qn 3 Instruction Design
Instruction length in multiples of 2 bytes
3 bits opcode
128 bytes of memory – 7 bit
5 registers – 3 bit
Fixed length
Stack
push @src
pop @dest
add
Instruction Length
3 + 7 = 10 bit
10 bit
3 bit
2 bytes

## Slide 25: Qn 3 Instruction Design
Stack
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
Older Value
Older Value
Older Value
Older Value
•
•
•
Top of stack
push @a0
push @a1
add
pop @a2
push @a0
push @a2
add
pop @a1
push @a1
push @a2
add
pop @a0
12 x 2 bytes = 24 bytes

## Slide 26: Qn 3 Instruction Design
Accumulator
load @src
add @src
store @dest
Instruction Length
3 + 7 = 10 bit
10 bit
10 bit
2 bytes
Instruction length in multiples of 2 bytes
3 bits opcode
128 bytes of memory – 7 bit
5 registers – 3 bit
Fixed length

## Slide 27: Qn 3 Instruction Design
Accumulator
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
Accumulator
Older Value
add @a0
store @a2
add @a2
store @a1
load @a1
add @a2
store @a0
7 x 2 bytes = 14 bytes

## Slide 28: Qn 3 Instruction Design
Mem-Mem
add @dest, @src1, @src2
Instruction Length
3 + 7 + 7 + 7 = 24 bit
24 / 8 = 3
↓
4 bytes
Instruction length in multiples of 2 bytes
3 bits opcode
128 bytes of memory – 7 bit
5 registers – 3 bit
Fixed length

## Slide 29: Qn 3 Instruction Design
Memory-Memroy
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
add @a0, @a1, @a2
add @a1, @a0, @a2
add @a2, @a0, @a1
3 x 4 bytes = 12 bytes

## Slide 30: Qn 3 Instruction Design
Reg-Reg
load $reg, @src
add $dest, $src1, $src2
store $reg, @dest
Instruction Length
3 + 3 + 7 = 13 bit
3 + 3 + 3 + 3 = 12 bit
3 +3 +7 = 13 bit
2 bytes
Instruction length in multiples of 2 bytes
3 bits opcode
128 bytes of memory – 7 bit
5 registers – 3 bit
Fixed length

## Slide 31: Qn 3 Instruction Design
Register-Register
a0 = a1 + a2
a1 = a0 + a2
a2 = a0 + a1
load $r1, @a1
load $r2, @a2
add $r0, $r1, $r2
store $r0, @a0
add $r1, $r0, $r2
store $r1, @a1
add $r2, $r0, $r1
store $r2, @a2
a0  $r0
a1  $r1
a2  $r2
8 x 2 bytes = 16 bytes

## Slide 32: Qn 3 Instruction Design
Notes: Memory-Memory is the most space efficient, but may not be the fastest, because each time we have to read from memory

## Slide 33: Q4 ISA Instruction Counts
Constraints
16-bit instructions
5-bit addresses
2 types of instructions:
Class A: one address
Class B: two addresses
Opcode
Address
Class A:
11 bit
5 bit
Opcode
Address
Class B:
6 bit
5 bit
Address
5 bit

## Slide 34: Q4 ISA Instruction Counts
Opcode
Address
Class A:
11 bit
5 bit
Opcode
Address
Class B:
6 bit
5 bit
Address
5 bit
Observations:
1. Opcode in Class B shouldn’t be a prefix of Class A
2. More Class B instructions  smaller total number of instructions

## Slide 35: Q4 ISA Instruction Counts
Opcode
Address
Class A:
11 bit
5 bit
Opcode
Address
Class B:
6 bit
5 bit
Address
5 bit
Min total number of instructions
Largest number of Class B instructions
(26 – 1) Class B instructions
one 6-bit prefix for Class A instructions
  1 x 25 Class A instructions
Total = (26 – 1) + (25) = 63 + 32 = 95
More Class B instructions  smaller total number of instructions
Addition

## Slide 36: Q4 ISA Instruction Counts
Opcode
Address
Class A:
11 bit
5 bit
Opcode
Address
Class B:
6 bit
5 bit
Address
5 bit
Max total number of instructions
Smallest number of Class B instructions
1 Class B instructions
(26 – 1) 6-bit prefix for Class A instructions
  (26 – 1) x 25 Class A instructions
Total = 1+ (26 – 1) x (25) = 1 + 2016 = 2017
More Class B instructions  smaller total number of instructions
Addition

## Slide 37: Q4 ISA Instruction Counts
Opcode
Address
Class A:
11 bit
5 bit
Opcode
Address
Class B:
6 bit
5 bit
Address
5 bit
Observations:
1. Opcode in Class B shouldn’t be a prefix of Class A
2. The presence of each Class B opcode eliminates 211-6 = 32 Class A opcode
There are 211 = 2048 Class A opcodes theoretically.
Min:
63 Class B, eliminating 63 x 32 = 2016 Class A opcodes
Total: 63 + (2048 – 2016) = 95
Subtraction

## Slide 38: Q4 ISA Instruction Counts
Opcode
Address
Class A:
11 bit
5 bit
Opcode
Address
Class B:
6 bit
5 bit
Address
5 bit
Observations:
1. Opcode in Class B shouldn’t be a prefix of Class A
2. The presence of each Class B opcode eliminates 211-6 = 32 Class A opcode
There are 211 = 2048 Class A opcodes theoretically.
Max:
1 Class B, eliminating 1 x 32 = 32 Class A opcodes.
Total: 1 + (2048 – 32) = 2017
Subtraction

## Slide 39: Backup:
Type A: 4-bit opcode
Type B: 8-bit opcode
Type C: 10-bit opcode
Find min and max number of instructions (with at least one instruction of each type).
Min:
Maximize A, then maximize B, leave the rest to C
A: 24 – 1 = 15, leave one 4-bit prefix to B and C
B: 1 x 28-4 – 1 = 15, leave one 8-bit prefix to C
C: 1 x 210-8 = 4
Total: 15 + 15 + 4 = 34
Max:
Minimize A, then minimize B, leave the rest of C
A: 1
B: 1
Each type A eliminates 28-4 = 16 type B, and 210-4 = 64 type C
Each type B eliminates 210-8 = 4 type C
C: 210 – 1 x 64 – 1 x 4 = 956
Total: 1 + 1 + 956 = 958
Min: addition
Max: subtraction
Notes: 0000 to A
0001 – 1111 to B and C
0001 0000 to B
0001 0001 – 0001 1111 to C, there are 15 x 4 = 60
The rest 4-bit prefix 0010 – 1111 are all for C, 14 x 64 = 896
A eliminate B is not used since we are guaranteed to have at least one type B. Still good to have a sanity check.

## Slide 40
Illustration
Type A: 4-bit opcode
Type B: 8-bit opcode
Type C: 10-bit opcode
Min: 34
0000 to 1110
Other fields
Type A:
1111
Type B:
0000 to 1110
Other fields
1111
Type C:
1111
Other fields
00 to 11
24 – 1= 15
1 x (24 – 1)= 15
1 x 1 x 22 = 4
0
4
8
10
0
4
8
0
4
Addition

## Slide 41
Illustration
Type A: 4-bit opcode
Type B: 8-bit opcode
Type C: 10-bit opcode
Min: 34
0000 to 1110
Other fields
Type A:
1111
Type B:
0000 to 1110
Other fields
1111
Type C:
1111
Other fields
00 to 11
24 – 1= 15
1 x (24 – 1)= 15
1 x 1 x 22 = 4
0
4
8
10
0
4
8
0
4
Subtraction:
Maximize A, then maximize B, leave the rest to C
Each type A eliminates 28-4 = 16 type B, and 210-4 = 64 type C
Each type B eliminates 210-8 = 4 type C
A: 24 – 1 = 15
B: 28 – 15 x 16 – 1 = 15
C: 210 – 15 x 64 – 15 x 4 = 4

## Slide 42
0000
Other fields
Type A:
0001
Type B:
0000
Other fields
0001
Type C:
0001 to 1111
Other fields
00 to 11
1
1 x 1 = 1
1 x (24 – 1) x 22 = 60
0010 to 1111
Type C:
000000 to 111111
Other fields
(24 – 2) x 26 = 896
0
4
8
10
0
4
10
0
4
8
0
4
Illustration
Type A: 4-bit opcode
Type B: 8-bit opcode
Type C: 10-bit opcode
Max: 958
Addition

## Slide 43
smaller: if (target < array[mid]):
finish smaller branch, skip the rest
else:
bigger: if (target > array[mid])
finish bigger branch, skip the rest
equal: else:
finish equal branch
Step 1: Rewrite
smaller: if not (target < array[mid]):
jump to bigger
(else:)
finish smaller branch, skip the rest
bigger: if not (target > array[mid]):
jump to equal
(else:)
finish bigger branch, skip the rest
equal: finish equal branch
slt to check target < array[mid],
we need it to be false (0) to jump
target > array[mid] is equivalent to array[mid] < target
we need it to be false (0) to jump
Digression: if we need a condition to be true (not 0), we use bne $t1, $0, label instead 
Step 2: Determine the conditions
Backup: C to MIPS

## Slide 44: CS2100 Tutorial 4
Song Kai
song.kai@u.nus.edu