## Slide 1: CS2100 Tutorial 6
Song Kai
song∙kai@nus∙edu.sg

## Slide 2: Boolean Algebra
Precedence: Not (') > And (.) > Or (+)
Duality: If the AND/OR operators and identity elements 0/1 in a Boolean equation are interchanged, it remains valid.
Identity laws | 
A + 0 = 0 + A = A | A ∙ 1 = 1 ∙ A = A
Inverse/complement laws | 
A + A' = 1 | A ∙ A' = 0
Commutative laws | 
A + B = B + A | A ∙ B = B ∙ A
Associative laws | 
A + (B + C) = (A + B) + C | A ∙ (B ∙ C) = (A ∙ B) ∙ C
Distributive laws | 
A ∙ (B + C) = (A ∙ B) + (A ∙ C) | A + (B ∙ C) = (A + B) ∙ (A + C)
Notes: Remember to write . for and

## Slide 3
Idempotency | 
X + X = X | X ∙ X = X
One element / Zero element | 
X + 1 = 1 | X ∙ 0 = 0
Involution | 
( X' )' = X | 
Absorption 1 | 
X + X∙Y = X | X∙(X + Y) = X
Absorption 2 | 
X + X'∙Y = X + Y | X∙(X' + Y) = X∙Y
DeMorgans' (can be generalised to more than 2 variables) | 
(X + Y)' = X' ∙ Y' | (X ∙ Y)' = X' + Y'
Consensus | 
X∙Y + X'∙Z + Y∙Z = X∙Y + X'∙Z | (X+Y)∙(X'+Z)∙(Y+Z) = (X+Y)∙(X'+Z)
Notes: Notice the pattern for absorption and consensus

## Slide 4: Q2 Boolean to Sum-of-Product (SOP)
F(x,y,z)
= (x + y∙z')∙(y' + y) + x'∙(y∙z' + y)
= (x + y∙z') ∙ 1 + x'∙y
Absorption 1 | 
X + X∙Y = X | X∙(X + Y) = X
Complement

## Slide 5: Q2 Boolean to Sum-of-Product (SOP)
F(x,y,z)
= (x + y∙z')∙(y' + y) + x'∙(y∙z' + y)
= (x + y∙z') ∙ 1 + x'∙y
= x + y∙z' + x'∙y
Identity laws | 
A + 0 = 0 + A = A | A ∙ 1 = 1 ∙ A = A

## Slide 6: Q2 Boolean to Sum-of-Product (SOP)
F(x,y,z)
= (x + y∙z')∙(y' + y) + x'∙(y∙z' + y)
= (x + y∙z') ∙ 1 + x'∙y
= x + y∙z' + x'∙y
= x + y + y∙z'
Absorption 2 | 
X + X'∙Y = X + Y | X∙(X' + Y) = X∙Y

## Slide 7: Q2 Boolean to Sum-of-Product (SOP)
F(x,y,z)
= (x + y∙z')∙(y' + y) + x'∙(y∙z' + y)
= (x + y∙z') ∙ 1 + x'∙y
= x + y∙z' + x'∙y
= x + y + y∙z'
= x + y
Absorption 1 | 
X + X∙Y = X | X∙(X + Y) = X

## Slide 8: SOP and POS
Put the right ticks in the following table∙
Expression | SOP? | POS?
X'∙Y + X∙Y' + X∙Y∙Z |  | 
(X+Y')∙(X'+Y)∙(X'+Z') |  | 
X' + Y + Z |  | 
X∙(W' + Y∙Z) |  | 
X∙Y∙Z' |  | 
W∙X'∙Y + V∙(X∙Z + W') |  | 












SOP expr: A product term or a logical sum (OR) of several product terms∙
POS expr: A sum term or a logical product (AND) of several sum terms∙

## Slide 9: 11. Minterms and Maxterms (2/2)
The minterms and maxterms on 2 variables are denoted by m0 to m3 and M0 to M3 respectively.
Each minterm is the complement of the corresponding maxterm
  Example: m2 = x∙y' m2' = ( x∙y' )' = x' + ( y' )' = x' + y = M2
x | y | Minterms |  | Maxterms | 
 |  | Term | Notation | Term | Notation
0 | 0 | x'∙y' | m0 | x+y | M0
0 | 1 | x'∙y | m1 | x+y' | M1
1 | 0 | x∙y' | m2 | x'+y | M2
1 | 1 | x∙y | m3 | x'+y' | M3

## Slide 10: Sum-of-Minterms and Product-of-Maxterms
Also called canonical SOP and canonical POS
Sum-of-minterms connects all conditions that makes the function 1 using OR.
Product-of-maxterms connects all conditions that makes the function 0 using AND.
x | y | z | F2 | F3
0 | 0 | 0 | 0 | x
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | x
F2 = x'∙y'∙z + x∙y'∙z' + x∙y'∙z + x∙y∙z' + x∙y∙z = m1 + m4 + m5 + m6 + m7 = Sm(1,4,5,6,7)
F2 = (x+y+z) ∙ (x+y'+z) ∙ (x+y'+z') = M0 ∙ M2 ∙ M3 = PM(0,2,3)
F3 = Sm(1,3,4,5) + Sd(0,7)
F3 = PM(2,6) ∙ Pd(0,7)

## Slide 11: Q2 Boolean to Sum-of-Product (SOP)
(b) G(p,q,r,s)
= (5, 9, 13)
= ( p + q' + r + s' ) ∙ ( p' + q + r + s' ) ∙ ( p' + q' + r + s' )
5 = 0101
m5 = p' ∙ q ∙ r' ∙ s
M5 = p + q' + r + s'
9 = 1001
m5 = p ∙ q' ∙ r' ∙ s
M5 = p' + q + r + s'
13 = 1101
m5 = p ∙ q ∙ r' ∙ s
M5 = p' + q' + r + s'

## Slide 12: Q2 Boolean to Sum-of-Product (SOP)
(b) G(p,q,r,s)
= (5, 9, 13)
= ( p + q' + r + s' ) ∙ ( p' + q + r + s' ) ∙ ( p' + q' + r + s' )
= ((q' + r + s') + (p . p ')) ∙ ( p' + q + r + s' )
= ((q' + r + s') + 0) ∙ ( p' + q + r + s' )
= (q' + r + s') ∙ ( p' + q + r + s' )
Distributive laws | 
A ∙ (B + C) = (A ∙ B) + (A ∙ C) | A + (B ∙ C) = (A + B) ∙ (A + C)
Inverse/complement laws | 
A + A' = 1 | A ∙ A' = 0
Identity laws | 
A + 0 = 0 + A = A | A ∙ 1 = 1 ∙ A = A
Notes: Let A = q' + r + s'

## Slide 13: Q2 Boolean to Sum-of-Product (SOP)
(b) G(p,q,r,s)
= (5, 9, 13)
= ( p + q' + r + s' ) ∙ ( p' + q + r + s' ) ∙ ( p' + q' + r + s' )
= (q' + r + s') ∙ ( p' + q + r + s' )
= (r + s') + (q' ∙ (p' + q))
Distributive laws | 
A ∙ (B + C) = (A ∙ B) + (A ∙ C) | A + (B ∙ C) = (A + B) ∙ (A + C)
Notes: Let A = r + s'

## Slide 14: Q2 Boolean to Sum-of-Product (SOP)
(b) G(p,q,r,s)
= (5, 9, 13)
= ( p + q' + r + s' ) ∙ ( p' + q + r + s' ) ∙ ( p' + q' + r + s' )
= (q' + r + s') ∙ ( p' + q + r + s' )
= (r + s') + (q' ∙ (p' + q))
= p'∙ q' + r + s'
Absorption 2 | 
X + X'∙Y = X + Y | X∙(X' + Y) = X∙Y
Notes: Let X = q’, Y = p’

## Slide 15: Logic Gates
a
b
ab
a
b
a+b
a
a'
a
b
(a+b)'
a
b
(ab)'
a
b
a  b
EXCLUSIVE OR
AND
OR
NOT
NAND
NOR
All input lines needs to be filled.
{AND, OR, NOT}, {NAND}, {NOR} are three complete sets of logic.

## Slide 16: SOP: 2-level AND-OR or NAND circuit
Example: F = AB + C'D + E
  Using 2-level AND-OR circuit
F
A
B
D
C
E
  Using 2-level NAND circuit
F
A
B
D
C
E
F
A
B
D
C
E
Notes: NOT is not considered as a level
x’ + y’ + z’ = (x.y.z)’

## Slide 17: POS: 2-level OR-AND or NOR circuit
Example: G = (A+B)  (C'+D)  E
  Using 2-level OR-AND circuit
  Using 2-level NOR circuit
G
A
B
D
C
E
G
A
B
D
C
E
G
A
B
D
C
E
Notes: x’.y’.z’ = (x+y+z)’

## Slide 18: 5.1 4-Variable K-maps (1/2)
m4
m5
m7
m6
m0
m1
m3
m2
m12
m13
m15
m14
m8
m9
m11
m10
There are 16 square cells in a 4-variable K-map.
Example: Let the variables be w, x, y, z.
w
y
00
01
11
10
00 01 11 10
z
wx
yz
x
Notes: determine variables
use grey code to make sure adjacent cells differ by exactly one literal

## Slide 19: 5.2 How to Use K-maps (7/7)
Examples of valid and invalid groupings.
1
1
1
1
1
1
1
1
P
1
1
1
1
1
1
1
1
P
P
1
1
1
1
1
1
1
1
1
1
1
1
1
1
O
1
1
1
1
1
1
O
Find largest rectangles containing 1s and X.
The rectangles may cross borders.
The length and width must be powers of 2.
1
X
C
A
00
01
11
10
00 01 11 10
B
CD
AB
X
1
X
D
1
1
X
0
0
0
0
0
0
0
0
Notes: Don’t-care conditions could be chosen to be either ‘1’ or ‘0’, depending on which choice results in a simpler expression.

## Slide 20: Quick Review Questions #2

5-3. Identify the prime implicants and essential prime implicants of the two K-maps below.
0
1
a
b
0
0
1
1
0
1
0
1
00 01 11 10
c
a
bc
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
D
1
1
1
1
1
1
1
1
1
3 PIs
2 EPIs
7 PIs
4 EPIs
0
0
0
0
0
Notes: PI: combining the maximum possible number of minterms from adjacent squares in the map
EPI: a prime implicant that includes at least one minterm that is not covered by any other prime implicant.

## Slide 21
Q1. Consensus theorem
x·y + x’·z + y·z = x·y + x’·z
z
x
y
1
0
0
0
1
1
1
0
x·y + x’·z + y·z
= x·y + x’·z + 1·y·z [identity law]
= x·y + x’·z + (x+x’)·y·z [complement law]
= x·y + x’·z + x·y·z + x’·y·z [distributive law]
= x·y + x·y·z + x’·z + x’·y·z [commutative law]
= (x·y + x·y·z) + (x’·z + x’·y·z) [associative law]
= x·y + x’·z [absorption theorem 1]

## Slide 22
Q3.
m0
A
B
C
D
m1
m5
m4
m2
m3
m7
m6
m10
m11
m15
m14
m8
m9
m13
m12
m1: 0001 = A’B’C’D
(a)

## Slide 23
Q3.
(b)
(c)
A
B
C
D
1
1
0
1
0
1
0
X
0
X
1
1
0
X
0
X
(d)
How many PIs?
(e)
How many EPIs?
T(A,B,C,D) = Sm(0,1,2,4,5,9) + SX(6,11,14,15).
T(A,B,C,D) = PM(3,7,8,10,12,13)  PX(6,11,14,15).
4 PIs
2 EPIs

## Slide 24
Q3.
(b)
(c)
A
B
C
D
1
1
0
1
0
1
0
X
0
X
1
1
0
X
0
X
(f)
Simplified SOP expression:
A'D'
+ A'C'
+ B'C'D
or
A'D' + A'C' + AB'D
EPIs must be present in your answer
T(A,B,C,D) = Sm(0,1,2,4,5,9) + SX(6,11,14,15).
T(A,B,C,D) = PM(3,7,8,10,12,13)  PX(6,11,14,15).

## Slide 25
Q3.
(b)
K-map for T’:
A
B
C
D
0
0
1
0
1
0
1
X
1
X
0
0
1
X
1
X
(g)
Simplified POS expression:
T’ = AD’ + CD + AB
T = (AD’ + CD + AB )’
= (A’+D)  (C’+D’)  (A’+B’)
T(A,B,C,D) = Sm(0,1,2,4,5,9) + SX(6,11,14,15).
T(A,B,C,D) = PM(3,7,8,10,12,13)  PX(6,11,14,15).
Notes: K-map always generates SOP, to get POS, get SOP for T’ and apply DeMorgan

## Slide 26
Q3.
(h)
T = A'D' + A'C' + B'C'D
2-level AND-OR circuit:
2-level NAND circuit:
T
A
B
C
D
A
B
C
D
T
Notes: Dots and straightlines

## Slide 27
Q4. (a)
K | L | M | N | X | Y | Z
0 | 0 | 0 | 0 |  |  | 
0 | 0 | 0 | 1 |  |  | 
0 | 0 | 1 | 0 |  |  | 
0 | 0 | 1 | 1 |  |  | 
0 | 1 | 0 | 0 |  |  | 
0 | 1 | 0 | 1 |  |  | 
0 | 1 | 1 | 0 |  |  | 
0 | 1 | 1 | 1 |  |  | 
K | L | M | N | X | Y | Z
1 | 0 | 0 | 0 |  |  | 
1 | 0 | 0 | 1 |  |  | 
1 | 0 | 1 | 0 |  |  | 
1 | 0 | 1 | 1 |  |  | 
1 | 1 | 0 | 0 |  |  | 
1 | 1 | 0 | 1 |  |  | 
1 | 1 | 1 | 0 |  |  | 
1 | 1 | 1 | 1 |  |  | 
d
0
0
0
0
1
0
0
X(K,L,M,N) = 1 if KL = MN, or 0 otherwise, where KL, MN are 2-bit unsigned integers.
Y(K,L,M,N) = 1 if KL  MN, or 0 otherwise, where KL, MN are 2-bit unsigned integers.
Z(K,L,M,N) = 1 if KLM < LMN, or 0 otherwise, where KLM, LMN are 3-bit unsigned integers.
0
0
1
0
0
0
0
1
d
1
1
1
0
1
1
1
0
0
1
1
0
0
0
1
d
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
Assume input 0000 will not occur.

## Slide 28
K | L | M | N | X | Y | Z
0 | 0 | 0 | 0 | d | d | d
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
K | L | M | N | X | Y | Z
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
K
M
L
N
d
0
0
0
1
0
0
0
0
1
0
0
1
0
0
0
X
X = K'LM'N + KL'MN’ + KLMN
Q4. (b)(c)(d)
KLMN = 0000  X = 0

## Slide 29
K | L | M | N | X | Y | Z
0 | 0 | 0 | 0 | d | d | d
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
K | L | M | N | X | Y | Z
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
K
M
L
N
d
1
1
0
1
1
0
0
1
1
1
0
1
1
0
0
Y
Y = MN + K'N + K'M + L'M
Q4. (b)(c)(d)
KLMN = 0000  Y = 0
Notes: We have one more PI not shown here, which is the first row

## Slide 30
K | L | M | N | X | Y | Z
0 | 0 | 0 | 0 | d | d | d
0 | 0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
K | L | M | N | X | Y | Z
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
K
M
L
N
d
1
1
0
0
1
0
0
0
0
1
1
1
1
0
0
Z
Z = K’
Q4. (b)(c)(d)
KLMN = 0000  Z = 1

## Slide 31: Assignment 2 Reminder
Due on 17 March, 1pm
3 attempts, latest submission
Format is very important:
  Datapath: Enter X for don’t-care
  Minterms and maxterms: list them out in increasing order, comma-separated, with no space or other punctuations, enclosed in round brackets.
    (1,2,3,4) (1,3,2,4) (1, 2, 3, 4) 1,2,3,4
  Simplified SOP and POS: use dot for AND, + for OR, single quote for NOT, without other symbols and unnecessary parenthesis.
    (A+B).(C+D) (A + B).(C+D) (A+B)(C+D)
  PI and EPI: Write EPIs before PIs, order within EPIs and within PIs do not matter.

## Slide 32: Backup: Quine-McCluskey for Q4 Y
0:0000
1:0001
2:0010
3:0011
5:0101
6:0110
7:0111
10:1010
11:1011
15:1111
0,1: 000-
0,2: 00-0
1,3: 00-1
1,5: 0-01
2,3: 001-
2,6: 0-10
2,10: -010
3,7: 0-11
3,11: -011
5,7: 01-1
6,7: 011-
7,15: -111
10,11:101-
11,15: 1-11
0,1,2,3: 00—
1,3,5,7: 0--1
2,3,6,7: 0-1-
2,3,10,11: -01-
3,7,11,15: --11

## Slide 33: CS2100 Tutorial 6
Song Kai
song∙kai@nus∙edu.sg