## Slide 1: CS2100 Tutorial 7
Song Kai
song.kai@nus.edu.sg

## Slide 2: 1. Introduction
Two classes of logic circuits
  Combinational
  Sequential
Combinational Circuit
  Each output depends entirely on the immediate (present) inputs.
Combinational
Logic
: :
inputs
outputs
: :
Sequential Circuit
  Each output depends on both present inputs and state.
Memory
Combinational
Logic
: :
inputs
outputs
: :

## Slide 3: 4. Gate-Level (SSI) Design: Half Adder (1/2)
Design procedure:
  1. State problem Example: Build a Half Adder.
  2. Determine and label the inputs and outputs of circuit. Example: Two inputs and two outputs labelled, as shown below.
  3. Draw the truth table.
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
X
Y
S
C
(X + Y)
Half
Adder

Notes: SSI Small Scale Integration
As opposed to medium scale integration

## Slide 4: 4. Gate-Level (SSI) Design: Half Adder (2/2)
  4. Obtain simplified Boolean functions. Example: C = X∙Y S = X'∙Y + X∙Y' = XY
  5. Draw the logic diagram.
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
X
Y
S
C
Half Adder
X
Y
S
C
(X + Y)
Half
Adder

Block diagram of Half Adder

## Slide 5: 5. Block-Level Design
More complex circuits can also be built using block-level method.
In general, block-level design method (as opposed to gate-level design) relies on algorithms or formulae of the circuit, which are obtained by decomposing the main problem to sub-problems recursively (until small enough to be directly solved by blocks of circuits).
Simple examples using 4-bit parallel adder as building blocks:
  1. BCD-to-Excess-3 Code Converter
  2. 16-bit Parallel Adder
  3. Adder cum Subtractor

## Slide 6: 5. 4-bit Parallel Adder (1/4)
Consider a circuit to add two 4-bit numbers together and a carry-in, to produce a 5-bit result.
4-bit
Parallel Adder
C5
C1
X2
X1
Y4
Y3
S4
S3
S2
S1
Y2
Y1
X4
X3
Black-box view of 4-bit parallel adder
5-bit result is sufficient because the largest result is: 11112 + 11112 + 12 = 111112

## Slide 7: 5. BCD to Excess-3 Converter: Revisit (2/2)
Block-level circuit:
4-bit Parallel Adder
X4
X3
X2
X1
Y4
Y3
Y2
Y1
0
0
1
1
S4
S3
S2
S1
BCD
code
Excess-3
code
unused
0
Cin
Cout
A BCD to Excess-3 Code Converter
Note: In the lab, input 0 (low) is connected to GND, 1 (high) to Vcc.

## Slide 8: 5. 16-bit Parallel Adder
Larger parallel adders can be built from smaller ones.
Example: A 16-bit parallel adder can be constructed from four 4-bit parallel adders:
4-bit // adder
X4..X1
Y4..Y1
C1
S4..S1
4-bit // adder
X8..X5
Y8..Y5
C5
S8..S5
4-bit // adder
X12..X9
Y12..Y9
C9
S12..S9
4-bit // adder
X16..X13
Y16..Y13
C13
S16..S13
C17
4
4
4
4
4
4
4
4
4
4
4
4
A 16-bit parallel adder
4
S4..S1
S4S3S2S1
=

## Slide 9
Q1.
D3. A combinational circuit takes in a 5-bit input ABCDE and generates a 2-bit value PQ such that PQ represents the distance between the two closest 1s in the input. The distance is defined to be the number of 0s between the two closest 1s.
You may assume that the distance is always determinable from the given input. Therefore, inputs such as 00000 and 01000 will not be supplied to this circuit.
You are to design a circuit to implement a function V(A,B,C,D,E) that takes in input ABCDE and generates output 1 if ABCDE is a valid input for the circuit in question D3 above, or 0 if ABCDE is an invalid input.

## Slide 10
Q1.
Cin
X
Y
Z
Carry
Sum
Full
Adder
Cin
Cin
X1
X0
Y1
Y0
2-bit
// adder
Cout
S1
S0
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
COMP
X<Y
X=Y
X>Y
Count the number of 1’s in ABCDE.
If > 1 then V = 1, else V = 0.
A
B
C
0
E
D
0
0
0
1
0
V
Important: All inputs must be connected to some value! Leave no inputs “hanging”.
Unused outputs may be left alone.
Notes:  Can we connect Carry and Sum of the full adder to X0 and X1 of the 2-bit adder respectively instead? Why?
 Can we connect E to Y1 and 0 to Y0 instead? Why?
 Can we swap D and E in the above diagram?

## Slide 11: Q2 Block Circuit Design
Add-1-Then-Half
Input: ABCD
Output: EFGH
Objective: EFGH = (ABCD + 1) / 2
Component: 4-bit parallel adder
Cin
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
// adder
Cout
S3
S2
S1
S0
Largest subscript: MSB
Smallest subscript: LSB

## Slide 12: Q2 Block Circuit Design
EFGH = (ABCD + 1) / 2
Get the Carry-Out and 3 MSBs
Note: All input needs to be filled.
Notes: Can I shift 1 from cin to y0?

## Slide 13: Q2 Block Circuit Design
EFGH = (ABCD + 1) / 2
A | B | C | D | E | F | G | H
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0

## Slide 14: Q2 Block Circuit Design
EFGH = (ABCD + 1) / 2
If D = 0,
ABC1 / 2 = 0ABC = 0ABC + D
If D = 1,
(ABC1 + 1) / 2 = 0ABC + 1 = 0ABC + D
Note: All input needs to be filled.

## Slide 15: Q2 Block Circuit Design
(b) 4221-to-8421
Input: PQRS
Output: WXYZ
Objective: Convert PQRS from 4221-to-8421, and store it in WXYZ
Component: Add-1-Then-Half Device

## Slide 16: Q2 Block Circuit Design
4221-to-8421
P | Q | R | S | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
Notes: 4221 and 8421 are weights at each digit
8421 is also binary coded decimal BCD

## Slide 17: Q2 Block Circuit Design
4221-to-8421
P | Q | R | S | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
Notes: Whether the number is odd or even purely depends on the least significant digit

## Slide 18: Q2 Block Circuit Design
4221-to-8421
P | Q | R | S | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
WXY = (PQR + 1) / 2

## Slide 19: Q2 Block Circuit Design
4221-to-8421
P | Q | R | S | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
WXY = (PQR + 1) / 2
Notes: PQR0 to WXY is wrong, but PQR1 to WXY is correct

## Slide 20
How do you implement a circuit that takes in a quaternary (base 4) digit A represented in 4-bit excess 3 code A3A2A1A0, and generates F3F2F1F0 which is A in excess 11 (eleven) code, without any logic gates?
20
Q3
 | Excess 3 |  |  |  | Excess 11 |  |  | 
0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0
2 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1
3 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
 | Excess 3 |  |  |  | Excess 11 |  |  | 
0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0
2 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1
3 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
F3F2F1F0 =
1A2A1A0
Remember: Logic constants 0 and 1 are always available.
Notes: Given a digit A, its excess 3 code is A+3, and its excess 11 code is A +11

## Slide 21
BCD code
21
Q4
Digits: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Code: | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001
Given two decimal digits A and B, represented by their BCD codes A3A2A1A0 and B3B2B1B0 respectively, implement a circuit without using any logic gates to calculate the BCD code of the 3-digit output of (51A) + (20(B%2)), where % is the modulo operator. Name the outputs F11F10F9F8 F7F6F5F4 F3F2F1F0.
A |  |  |  | 5A |  |  |  |  |  |  | 
A3 | A2 | A1 | A0 |  |  |  |  |  |  |  | 
Hint: Fill in the table on the right.

## Slide 22
BCD code
22
Q4
Digits: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Code: | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001
A |  |  |  | 5A |  |  |  |  |  |  | 
A3 | A2 | A1 | A0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1
5A = (10A) / 2

## Slide 23
BCD code
23
Q4
Digits: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Code: | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001
A |  |  |  | 5A |  |  |  |  |  |  | 
A3 | A2 | A1 | A0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1
A3
A2
A1
A0
0
A0
A0
0
0
0
A3
A2
A1

## Slide 24
24
Q4
5A
50A
A3
A2
A1
A0
0
A0
A0
0
0
0
A3
A2
A1
0
0
0
0
51A

## Slide 25
25
Q4
5A
50A
A3
A2
A1
A0
0
A0
A0
0
0
0
A3
A2
A1
51A
A3
A2
A1
A0
51A + (20(B%2))
Notes: B % 2: we just look at its LSB

## Slide 26
26
Q4
5A
50A
A3
A2
A1
A0
0
A0
A0
0
0
0
A3
A2
A1
51A
A3
A2
A1
A0
51A + (20(B%2))
B3
B2
B1
B0
B0

## Slide 27: 8. Magnitude Comparator (2/4)
Let A = A3A2A1A0 , B = B3B2B1B0; xi = Ai∙Bi + Ai'∙Bi'
A2
B2
A3
B3
A0
B0
A1
B1
(A < B)
(A > B)
(A = B)
x3
x2
x1
x0
A3'∙B3
A3∙B3'
A3'∙B3 + x3∙A2'∙B2
+ x3∙x2.A1'∙B1
+ x3∙x2∙x1∙A0'∙B0
A3∙B3' + x3∙A2∙B2'
+ x3∙x2∙A1∙B1'
+ x3∙x2∙x1∙A0∙B0'
x3∙x2∙x1∙x0

Note:
xi = 1 only when Ai = Bi

## Slide 28: 8. Magnitude Comparator (4/4)

A function F accepts a 4-bit binary value ABCD, and returns 1 if 3  ABCD  12, or 0 otherwise. How would you implement F using magnitude comparators and a suitable logic gate?
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A
B
C
D
0
0
1
0
1
1
0
1
F
ABCD > 2 and ABCD < 13

## Slide 29: Q5 Magnitude Comparator
(a) F(A, B, C, D) =

## Slide 30: Q5 Magnitude Comparator
(a) F(A, B, C, D) =
m12: A.B.C’.D’
m13: A.B.C’.D
m14: A.B.C.D’
m15: A.B.C.D
ABCD > 11

## Slide 31: Q5 Magnitude Comparator
(a) F(A, B, C, D) =
= A ∙ B
When A = B = 1, F = 1; Otherwise F = 0

## Slide 32: Q5 Magnitude Comparator
(a) F(A, B, C, D) =
= A ∙ B
When A = B = 1, F = 1; Otherwise F = 0
ABCD >= 1100 > 1011

## Slide 33: Q5 Magnitude Comparator
(b) G(A, B, C, D) =
Palindromes
A | B | C | D | G
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 34: Q5 Magnitude Comparator
(b) G(A, B, C, D) =
Palindromes

## Slide 35: Q5 Magnitude Comparator
(c) H(A, B, C, D) =
B == C  H = 1
A | B | C | D | H
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 36: Q5 Magnitude Comparator
(c) H(A, B, C, D) =
B == C  H = 1
1
1
1
1
1
1
1
1
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
H = B.C + B’.C’

## Slide 37: Q5 Magnitude Comparator
A | B | C | D | Z
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
(d) Z(A, B, C, D) =
Easy if m15 is in Z
Find a way to include all with D = 1 except m15

## Slide 38: Q5 Magnitude Comparator
A | B | C | D | Z
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
(d) Z(A, B, C, D) =
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
COMP
X<Y
X=Y
X>Y
D
D
D
D
A
B
C
D
Z

## Slide 39: Q5 Magnitude Comparator
A | B | C | D | Z
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
(d) Z(A, B, C, D) =
Notes: When D=1, DABC equals to ABCD only when A=B=C=1. If we express ABCD and DABC in decimal, we get 8A+4B+2C+1 and 8+4A+2B+C. By equating them, we get 7 = 4A+2B+C, which is only valid when A, B and C are 1. In any other cases, ABCD < DABC i.e. X<Y.
When D = 0, DABC equals to ABCD only when A=B=C=0. In any other cases, ABCD > DABC i.e. X>Y.

## Slide 40: 9. Circuit Delays (2/5)
As a simple example, consider the full adder circuit where all inputs are available at time 0. Assume each gate has delay t.
Outputs S and C experience delays of 2t and 3t respectively.
max(0,0)+t = t
t
X
Y
S
C
Z
0
0
0
max(t,0)+t = 2t
max(t,2t)+t = 3t
2t

## Slide 41: CS2100 Tutorial 7
Song Kai
song.kai@nus.edu.sg