## Slide 1: CS2100 Tutorial 8
Song Kai
song.kai@nus.edu.sg

## Slide 2: Demultiplexers
Example: 1-to-4 demultiplexer.
demux
Data D
Outputs
select
S1 S0
Y0 = D∙S1'∙S0'
Y1 = D∙S1'∙S0
Y2 = D∙S1∙S0'
Y3 = D∙S1∙S0
Input | Output | Purpose
Data D Select lines Sn-1, Sn-2, …, S0 | D to line Yi = Sn-1Sn-2…S0 0 to rest of the lines | Direct data from input to one selected output line.

## Slide 3: Multiplexers
Input | Output | Purpose
2n inputs I0, I1, … I2n-1 Select lines Sn-1, Sn-2, …, S1, S0 | 1 output Ii among 2n inputs, Ii = Sn-1Sn-2…S1 S0 | Select 1 data as output among 2n inputs based on n selection lines
Truth table for a 4-to-1 multiplexer:
4:1
mux
Y
Inputs
select
S1 S0
I0
I1
I2
I3
4:1
MUX
Y
Inputs
select
S1 S0
I0
I1
I2
I3
0
1
2
3
Output

## Slide 4: Multiplexers
Output of multiplexer is
  “sum of the (product of data lines and selection lines)”
Example: Output of a 4-to-1 multiplexer is:
  Y = ?
I0∙(S1'∙S0') + I1∙(S1'∙S0) + I2∙(S1∙S0') + I3∙(S1∙S0)
Note:
Expressing
I0∙(S1'∙S0') + I1∙(S1'∙S0) + I2∙(S1∙S0') + I3∙(S1∙S0)
in minterms notation, it is equal to
I0∙m0 + I1∙m1 + I2∙m2 + I3∙m3
This is useful later.

## Slide 5: Multiplexers: Implementing Functions
F(A,B,C) = S m(1,3,5,6)
mux
A B C
0
1
2
3
4
5
6
7
0
1
0
1
0
1
1
0
F
This method works because:
Output = I0m0 + I1m1 + I2m2 + I3m3 + I4m4 + I5m5 + I6m6 + I7m7
Supplying '1' to I1,I3,I5,I6 , and '0' to the rest:
Output = m1 + m3 + m5 + m6
From slide 4:1 mux
Expressing
I0∙(S1'∙S0') + I1∙(S1'∙S0) + I2∙(S1∙S0') + I3∙(S1∙S0)
in minterms notation, it is equal to
I0∙m0 + I1∙m1 + I2∙m2 + I3∙m3
Notes: At each input ABC, we decide what is the output.

## Slide 6: Constructing Larger Multiplexers
Another implementation of an 8-to-1 multiplexer using smaller multiplexers:
4:1 MUX
S2 S1
I0
I1
2:1 MUX
S0
I2
I3
2:1 MUX
S0
I4
I5
2:1 MUX
S0
I6
I7
2:1 MUX
S0
Y
I0
When
S2S1S0 = 000
I0
I4
I2
I6
Q: Can we use only 2:1 multiplexers?
0
0
0
0
0 0
S2S1S0 = 101
1
1
1
1
1 0
I1
I5
I3
I7
I5

## Slide 7: Using Smaller Multiplexers

  3. Draw the truth table for function, by grouping inputs by selection line values, then determine multiplexer inputs by comparing input line (C) and function (F) for corresponding selection line values.
mux
A B
0
1
2
3
1
0
F
C
A | B | C | F | MUX input
0 | 0 | 0 | 1 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 
1
C
0
C'

## Slide 8: 5. Using Smaller Multiplexers (5/6)

Alternative: What if we use A for input lines, and B, C for selector lines?
A' (when BC = 00)
A' (when BC = 01)
A (when BC = 10)
A' (when BC = 11)
mux
B C
0
1
2
3
A
F
mux
B C
0
1
2
3
?
?
?
?
F

## Slide 9: Q1 Multiplexer Realization
F(X,Y,Z) = P M(1,5,6) ∙ P D(4) =
X | Y | Z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | d
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Larger subscript  More significant bit

## Slide 10: Q1 Multiplexer Realization
F(X,Y,Z) = P M(1,5,6) ∙ D(4)
X | Y | Z | F | 
0 | 0 | 0 | 1 | Z'
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 
1 | 0 | 0 | D | 0 / Z'
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 0 | Z
1 | 1 | 1 | 1 | 
0
1
2
3
4:1
MUX
0
1
F
X
Y
Z'
1
0
Z

## Slide 11: Q1 Multiplexer Realization
F(X,Y,Z) = P M(1,5,6) ∙ D(4)
X | Y | Z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | D
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Y | Z | X | F | 
0 | 0 | 0 | 1 | X' / 1
0 | 0 | 1 | D | 
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 1 | X'
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 
0
1
2
3
4:1
MUX
0
1
F
Y
Z
1
0
X'
1

## Slide 12: Decoders
Example: If codes 00, 01, 10, 11 are used to identify four light bulbs, we may use a 2-bit decoder.
2x4
DEC
2-bit code
X
Y
F0 F1 F2 F3
Bulb 0
Bulb 1
Bulb 2
Bulb 3
This is a 24 decoder which selects an output line based on the 2-bit code supplied.
Truth table:
X | Y | F0 | F1 | F2 | F3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 13: Decoders
From truth table, circuit for 24 decoder is:
F0 = X'Y'
F1 = X'Y
F2 = XY'
F3 = XY
X
Y
Note: Each output is a minterm (X'Y', X'Y, XY' or XY) of a 2-variable function
X | Y | F0 | F1 | F2 | F3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 14: Decoders with Enable
Decoders often come with an enable control signal, so that the device is only activated when the enable, E = 1.
Truth table:
Circuit of a 24 decoder with enable:
X
Y
F0 = EX'Y'
F1 = EX'Y
F2 = EXY'
F3 = EXY
E
E | X | Y | F0 | F1 | F2 | F3
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
0 | d | d | 0 | 0 | 0 | 0

## Slide 15: 2. Decoders with Enable (2/2)
In the previous slide, the decoder has a one-enable control signal, i.e. the decoder is enabled with E=1.
In most MSI decoders, enable signal is zero-enable, usually denoted by E' or Ē. The decoder is enabled when the signal is zero (low).
Decoder with 1-enable
Decoder with 0-enable
E | X | Y | F0 | F1 | F2 | F3
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
0 | d | d | 0 | 0 | 0 | 0
E' | X | Y | F0 | F1 | F2 | F3
0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1
1 | d | d | 0 | 0 | 0 | 0

## Slide 16: Decoders
Input | Output | Purpose
Select lines Sn-1, Sn-2, …, S1, S0 1 enable line | If enabled: 1 to line Fi=Sn-1Sn-2…S1S0 0 to rest of the lines If not enabled: 0 to all lines | Pick one line out of 2n lines
2x4
DEC
2-bit code
X
Y
F0 F1 F2 F3
Bulb 0
Bulb 1
Bulb 2
Bulb 3
E

## Slide 17: Decoders: Implementing Functions Revisit
Example: Implement the following function using a 38 decoder and an appropriate logic gate
  f(Q,X,P) =  m(0,1,4,6,7) =  M(2,3,5)
We may implement the function in several ways:
  Using a decoder with active-high outputs with an OR gate: f(Q,X,P) = m0 + m1 + m4 + m6 + m7
  Using a decoder with active-low outputs with a NAND gate: f(Q,X,P) = (m0'  m1'  m4'  m6'  m7' )'
  Using a decoder with active-high outputs with a NOR gate: f(Q,X,P) = (m2 + m3 + m5 )' [ = M2  M3  M5 ]
  Using a decoder with active-low outputs with an AND gate: f(Q,X,P) = m2'  m3'  m5'

## Slide 18: Decoders: Implementing Functions Revisit
f(Q,X,P) = Sm(0,1,4,6,7) =  M(2,3,5)
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
f(Q,X,P)
(a) Active-high decoder with OR gate.
f(Q,X,P)
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
(b) Active-low decoder with NAND gate.
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
f(Q,X,P)
(c) Active-high decoder with NOR gate.
f(Q,X,P)
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
(d) Active-low decoder with AND gate.
(m0'·m1'·m4'·m6'·m7)'
=m0+m1+m4+m6+m7
(m2+m3+m5)'
= m2'·m3'·m5'
= M2·M3·M5
m2'·m3'·m5'
= M2·M3·M5
Active-low  negated output

## Slide 19: Constructing Larger Decoders
Larger decoders can be constructed from smaller ones.
Example: A 38 decoder can be built from two 24 decoders (with one-enable) and an inverter.
3x8
DEC
S2
S1
S0
w
x
y
0
1
:
:
7
F0 = w'x'y'
F1 = w'x'y
:
:
F7 = wxy
2x4
DEC
S1
S0
0
1
2
3
F0 = w'x'y'
F1 = w'x'y
F2 = w'xy'
F3 = w'xy
E
2x4
DEC
S1
S0
0
1
2
3
F4 = wx'y'
F5 = wx'y
F6 = wxy'
F7 = wxy
E
w
x
y

## Slide 20: Constructing Larger Decoders
Construct a 416 decoder from two 38 decoders with one-enable and an inverter.
4x16
DEC
S3
S2
S1
S0
w
x
y
z
0
1
:
:
15
F0
F1
:
:
F15
3x8
DEC
S2
S1
S0
0
1
:
7
F0
F1
:
F7
E
3x8
DEC
S2
S1
S0
0
1
:
7
F8
F9
:
F15
E
w
x
y
z
Note: The input w and its complement w' are used to select either one of the two smaller decoders.

## Slide 21: Q2 Decoder Realization
K(W,X,Y,Z) = S m(8,11)
one-enabled 2x4 decoder with normal outputs
Cin
S1
24
DEC
0
1
2
3
S0
E
K
Cin
S1
24
DEC
0
1
2
3
S0
E
W
X
1
Y
Z
WXYZ = 1000 or 1011
WX is always 10
YZ is either 00 or 11
Notes: 8 = 1000
11 = 1011
WX need to be 10
YZ can be either 00 or 11
It is only when WX is 10 then the second decode is enabled

## Slide 22: Q2 Decoder Realization
K(W,X,Y,Z) = S m(8,11)
one-enabled 2x4 decoder with normal outputs
Cin
S1
24
DEC
0
1
2
3
S0
E
WXYZ = 1000 or 1011
WX is always 10
YZ is either 00 or 11
W
X
K
Alternatives:
X to S0
Y XOR Z
Notes: 8 = 1000
11 = 1011
WX need to be 10
YZ can be either 00 or 11
It is only when WX is 10 then the second decode is enabled
Take note of the cue for XNOR

## Slide 23: Encoders
Contains 2n (or fewer) input lines and n output lines.
Implemented with OR gates.
Example:
4-to-2 Encoder
F0
F1
F2
F3
D0
D1
Select via switches
2-bits code
Input | Output | Purpose
2n input lines with exactly one 1 | n bit output representing the input with value 1 | Give an encoding to based on the 2n input
Not including priority encoders!

## Slide 24: Encoders
Truth table:

With K-map, we obtain:
  D0 = F1 + F3 D1 = F2 + F3
Circuit:
F0
F1
F2
F3
D1
D0
Simple 4-to-2 encoder

## Slide 25: Priority Encoders
A priority encoder is one with priority
  If two or more inputs or equal to 1, the input with the highest priority takes precedence.
  If all inputs are 0, this input combination is considered invalid.
Example of a 4-to-2 priority encoder:
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | f | g | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
X | 1 | 0 | 0 | 0 | 1 | 1
X | X | 1 | 0 | 1 | 0 | 1
X | X | X | 1 | 1 | 1 | 1

## Slide 26: 3. Priority Encoders (2/2)
Understanding “compact” function table
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | f | g | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
X | 1 | 0 | 0 | 0 | 1 | 1
X | X | 1 | 0 | 1 | 0 | 1
X | X | X | 1 | 1 | 1 | 1
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | f | g | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Exercise: Obtain the simplified expressions for f, g and V.


## Slide 27: MSI Summary
 | Input | Output | Purpose
Encoders | 2n input lines with exactly one 1 | n bit output representing the input with value 1 | Give an encoding to based on the 2n input
Priority Encoders | 2n input lines with some 1s | n bit output representing the input with value 1 of highest priority | Give an encoding to based on the 2n input
Decoders | Select lines Sn-1, Sn-2, …, S1, S0 1 enable line | If enabled: 1 to line Fi=Sn-1Sn-2…S1S0 0 to rest of the lines If not enabled: 0 to all lines | Picks one line out of 2n lines
Multiplexers | 2n inputs I0, I1, … I2n-1 Select lines Sn-1, Sn-2, …, S1, S0 | 1 output Ii among 2n inputs, Ii = Sn-1Sn-2…S1 S0 | Select 1 data as output among 2n inputs based on n selection lines
Demultiplexers | Data D Select lines Sn-1, Sn-2, …, S1, S0 | D to line Yi = Sn-1Sn-2…S0 0 to rest of the lines | Direct data from input to one selected output line.

## Slide 28: Q3 Converter Design
A | B | C | D | F | G | H
0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1
When A = 1, FGH = #1s in ABCD
When A = 0,
FGH = 4 + #0s in ABCD
FGH = 2 x #0s in ABCD + #1s in ABCD

## Slide 29: Q3 Converter Design
When A = 1, FGH = #1s in ABCD
When A = 0,
FGH = 4 + #0s in ABCD
No. of 0s + 4
No. of 1s
Selection line comes from value of A

## Slide 30: Q3 Converter Design
When A = 1, FGH = #1s in ABCD
When A = 0,
FGH = 2 x #0s in ABCD + #1s in ABCD
2x No. of 0s + No. of 1s
No. of 1s
Selection line comes from value of A

## Slide 31
Q4.
The circuit on the left below comprises a 2-bit parallel adder and a 4:1 multiplexer. Fill in the table on the right. Each entry in the table is a simplified SOP expression for .
A | B | G(A,B,C,D)
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
4:1
MUX
0
1
2
3
S0
S1
G
2-bit
Adder
Cin
Cout
X1
X0
Y1
Y0
S1
S0
A
B
C
D
0
1
A | B | C | D | Cout | S1 | S0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
0
C’D + CD’
D
1

## Slide 32
Q4.
The circuit on the left below comprises a 2-bit parallel adder and a 4:1 multiplexer. Fill in the table on the right.
Each entry in the table is a simplified SOP expression for .
A | B | G(A,B,C,D)
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
4:1
MUX
0
1
2
3
S0
S1
G
2-bit
Adder
Cin
Cout
X1
X0
Y1
Y0
S1
S0
A
B
C
D
0
1
0
C’D + CD’
D
1
Selection lines: AB
When A = B = 0, Cout is selected, which is always 0.
G = 0
When A = 0, B = 1, S1 is selected. Consider different CD values.
If CD = 00 / 11, AB + CD = 01/100, S1 = 0
If CD = 01 / 10, AB + CD = 10 / 11, S1 = 1
G = C XOR D = C’.D + C.D’
When A = 1, B = 0, S0 is selected. Consider different CD values,
If CD = 00 / 10, AB + CD = 10 / 100, S0 = 0
If CD = 01 / 11, AB + CD = 11 / 101, S0 = 1
G = D
When A = B = 1, input 3 is always 1.
G = 1
Notes: XOR is not part of SOP

## Slide 33
Q4.
The circuit on the left below comprises a 2-bit parallel adder and a 4:1 multiplexer. Fill in the table on the right.
Each entry in the table is a simplified SOP expression for .
A | B | G(A,B,C,D)
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
4:1
MUX
0
1
2
3
S0
S1
G
2-bit
Adder
Cin
Cout
X1
X0
Y1
Y0
S1
S0
A
B
C
D
0
1
0
C’D + CD’
D
1
For each row, derive the simplified SOP expression for G as a function of C and D only

## Slide 34
Q5.
The circuit below uses an 8-3 priority encoder whose function is described in the table. What are the simplified SOP expressions for and ?
F7 | F6 | F5 | F4 | F3 | F2 | F1 | F0 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | X | X | X
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | X | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 1 | X | X | 0 | 1 | 0
0 | 0 | 0 | 0 | 1 | X | X | X | 0 | 1 | 1
0 | 0 | 0 | 1 | X | X | X | X | 1 | 0 | 0
0 | 0 | 1 | X | X | X | X | X | 1 | 0 | 1
0 | 1 | X | X | X | X | X | X | 1 | 1 | 0
1 | X | X | X | X | X | X | X | 1 | 1 | 1
F7
F6
F5
F4
F3
F2
F1
F0
8-to-3 priority
encoder
Y2
Y1
Y0
A
B
C
1
H2(A,B,C)
H1(A,B,C)
H0(A,B,C)
A | B | C | F7 | F6 | F5 | F4 | F3 | F2 | F1 | F0 | H2 | H1 | H0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 |  |  | 
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 |  |  | 
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 |  |  | 
1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 |  |  | 
1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 |  |  | 
1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 |  |  | 
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  |  | 
0 0 1
0 1 1
1 0 1
1 0 1
1 1 1
1 1 1
1 1 1
1 1 1
H2 = A + B
H1 = A + B’C
H0 = 1
Notes: F6, F4, F2, F0 they do not matter

## Slide 35: Assignment 2 Feedback
Q1
RR1 / RR2: 21 / $21 / $s5 are accepted.
Do take note of
base, e.g. 0b____, 0x____
number of bits, e.g. Instruction[31-26]* has 6 bits, and Instruction[25-21]* has 5 bits
Q2(b)
The last step is by the zero element theorem. Not by identity or annihilation.
There are multiple names for the same Boolean laws / theorems. Do use the ones given in CS2100.
Q2(c): How many minterms does a 2-literal product term in 𝐹 have
Why 40?

## Slide 36: Assignment 2 Feedback
Q4(b): There are only two EPIs for Z.
Q4(d)
All EPIs need to be written before PIs.
Don’t miss the dot (.)
Q4(e): Some of you have all the literals inverted.
Q5(c): We should have some don't-care terms for P.
Q5(e): Another alternative is (A XNOR B) NAND (C XNOR D)
Careless Mistakes:
Extra right bracket at the end (A XOR B).(C XOR D))
Extra zeros e.g. 000000E98
The single quote copied from other sources may not be displayed correctly in Canvas.
Notes: Errata all expressions can be written as both SOP and POS

## Slide 37: CS2100 Tutorial 8
Song Kai
song.kai@nus.edu.sg