## Slide 1: CS2100 Tutorial 9
Song Kai
song.kai@nus.edu.sg

## Slide 2: 1. Introduction (1/2)
Two classes of logic circuits
  Combinational
  Sequential
Combinational Circuit
  Each output depends entirely on the immediate (present) inputs.
Combinational
Logic
: :
inputs
outputs
: :
Sequential Circuit
  Each output depends on both present inputs and state.
Memory
Combinational
Logic
: :
inputs
outputs
: :

## Slide 3: 2. Memory Elements (3/3)
Two types of triggering/activation
  Pulse-triggered
  Edge-triggered
Pulse-triggered
  Latches
  ON = 1, OFF = 0
Edge-triggered
  Flip-flops
  Positive edge-triggered (ON = from 0 to 1; OFF = other time)
  Negative edge-triggered (ON = from 1 to 0; OFF = other time)
Positive edges
Negative edges
Positive pulses

## Slide 4: 3.1 S-R Latch
Characteristic table for active-high input S-R latch:
S
R
Q
Q'
Q(t+1) = ?

S + R'∙Q
S∙R = 0
Notes: set, reset

## Slide 5: 3.1 Gated S-R Latch
S-R latch + enable input (EN) and 2 NAND gates  a gated S-R latch.
S
R
Q
Q'
EN
S
EN
R
Q
Q'
Outputs change (if necessary) only when EN is high.
Notes: It can be 1-enable or 0-enable. In the diagram we have an 1-enable.

## Slide 6: 4. Flip-flops (FF)
S-R flip-flop, D flip-flop, and J-K flip-flop.
Note the “>” symbol at the clock input.
S
C
R
Q
Q'
D
C
Q
Q'
J
C
K
Q
Q'
Positive edge-triggered flip-flops
S
C
R
Q
Q'
D
C
Q
Q'
J
C
K
Q
Q'
Negative edge-triggered flip-flops
Positive edges
Negative edges
Positive pulses

## Slide 7: 4.1 S-R Flip-flop
S-R flip-flop: On the triggering edge of the clock pulse,
  R = HIGH and S = LOW  Q becomes LOW (RESET state)
  S = HIGH and R = LOW  Q becomes HIGH (SET state)
  Both R and S are LOW No change in output Q
  Both R and S are HIGH Invalid!
X = irrelevant (“don't care”)
 = clock transition LOW to HIGH
S
C
R
Q
Q'
Characteristic table of positive edge-triggered S-R flip-flop:
S-R for set-reset
Notes: set reset

## Slide 8: 4.2 D Flip-flop
D flip-flop: Single input D (data). On the triggering edge of the clock pulse,
  D = HIGH  Q becomes HIGH (SET state)
  D = LOW  Q becomes LOW (RESET state)
Hence, Q “follows” D at the clock edge.
A positive edge-triggered D flip-flop formed with an S-R flip-flop.
S
C
R
Q
Q'
CLK
D
 = clock transition LOW to HIGH
Convert S-R flip-flop into a D flip-flop: add an inverter.
D for Data or Delay
Handling data
Delay the data change to synchronize with the clock

## Slide 9: 4.3 J-K Flip-flop
J-K flip-flop circuit:
J
Q
Q'
CLK
Pulse transition detector
K
Characteristic table:
Q(t+1) = ?
J∙Q' + K'∙Q

Invented by Jack Kilby

## Slide 10: 4.4 T Flip-flop
T flip-flop: Single input version of the J-K flip-flop, formed by tying both inputs together.
Characteristic table:
T
Q
Q'
CLK
Pulse transition detector
J
C
K
Q
Q'
CLK
T
Q(t+1) = ?

T∙Q' + T'∙Q
T for toggle

## Slide 11: 5. Asynchronous Inputs (2/2)
A J-K flip-flop with active-low PRESET and CLEAR asynchronous inputs.
J
Q
Q'
CLK
Pulse transition detector
K
PRE
CLR
J
C
K
Q
Q'
PRE
CLR
PRE
CLR
CLK
Q
Preset
Toggle
Clear
J = K = HIGH
Notes: We use active low here: when PRESET is 0, the output is always 1; when CLEAR is 0, the output is always 0. They cannot be both zero, but can be both one.

## Slide 12: 6.1 Flip-flop Characteristic Tables
Each type of flip-flop has its own behaviour, shown by its characteristic table.

## Slide 13: 6.2 Sequential Circuits: Analysis
Example using D flip-flops
State equations:
A+ = A∙x + B∙x
B+ = A'∙x
Output function:
y = (A + B)∙x'
Figure 1
A
A'
B
B'
y
x
CP
D
Q
Q'
D
Q
Q'

## Slide 14: 6.2 Sequential Circuits: Analysis
State table for circuit of Figure 1:
State equations:
A+ = A∙x + B∙x
B+ = A'∙x
Output function:
y = (A + B)∙x'

## Slide 15: 6.2 Sequential Circuits: Analysis
State diagram of the circuit of Figure 1:
00
01
11
10
1/0
1/0
1/0
0/1
0/1
0/0
1/0
0/1
DONE!
Notes: We use x / y to indicate the input / output

## Slide 16: Q1 Circuit Analysis – T & D Flip-Flops
A'
B'
A'+B
(A’+B)’= A∙B'
A⊕B'

## Slide 17: Q1 Circuit Analysis – T & D Flip-Flops
Present State |  | Output | Flip-flop inputs |  | Next State | 
A | B | P = A⊕B' | TA = A∙B' | DB = A'+B | A+ | B+
0 | 0 | 1 | 0 | 1 |  | 
0 | 1 | 0 | 0 | 1 |  | 
1 | 0 | 0 | 1 | 0 |  | 
1 | 1 | 1 | 0 | 1 |  | 

## Slide 18: Q1 Circuit Analysis – T & D Flip-Flops
Present State |  | Output | Flip-flop inputs |  | Next State | 
A | B | P = A⊕B' | TA = A∙B' | DB = A'+B | A+ | B+
0 | 0 | 1 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 1 | 0 | 
1 | 0 | 0 | 1 | 0 | 0 | 
1 | 1 | 1 | 0 | 1 | 1 | 

## Slide 19: Q1 Circuit Analysis – T & D Flip-Flops
Present State |  | Output | Flip-flop inputs |  | Next State | 
A | B | P = A⊕B' | TA = A∙B' | DB = A'+B | A+ | B+
0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1 | 1 | 1

## Slide 20: Q1 Circuit Analysis – T & D Flip-Flops
Cycle | Cycle 1 | Cycle 2 | Cycle 3
State | 00 | 01 | 01
Output | 1 | 0 | 0
After 3 clock cycles, we are at state 1, with output 100.
No. of sinks?
2 sinks: State 1 & 3
Unused state?
State 3

## Slide 21: 6.4 Sequential Circuits: Design
Design procedure:
  Start with circuit specifications – description of circuit behaviour, usually a state diagram or state table.
  Derive the state table.
  Perform state reduction if necessary.
  Perform state assignment.
  Determine number of flip-flops and label them.
  Choose the type of flip-flop to be used.
  Derive circuit excitation and output tables from the state table.
  Derive circuit output functions and flip-flop input functions.
  Draw the logic diagram.

## Slide 22: 6.3 Flip-flop Excitation Tables (1/2)
Excitation tables: given the required transition from present state to next state, determine the flip-flop input(s).
JK Flip-flop
SR Flip-flop
D Flip-flop
T Flip-flop
characteristic table of JK Flip-flop
Notes: Given the transition from Q to Q+, what is the required flip-flop inputs to make it happen?

## Slide 23: 6.4 Design: Example #1 (1/5)

Given the following state diagram, design the sequential circuit using JK flip-flops.
00
10
11
0
0
0
0
1
1
1
1
01
Two flip-flops. Let's call them A and B.
One input variable. Let's call it x.

## Slide 24: 6.4 Design: Example #1 (2/5)

Circuit state/excitation table, using JK flip-flops.
00
10
11
0
0
0
0
1
1
1
1
01
JK Flip-flop's
excitation table.
0 X
0 X
1 X
0 X
X 0
X 0
X 0
X 1
0 X
1 X
X 1
X 0
0 X
1 X
X 0
X 1

## Slide 25: 6.4 Design: Example #1 (4/5)
From state table, get flip-flop input functions.
A
B
0
1
00 01 11 10
x
A
Bx
X
X
X
X
1
JA = B∙x'
JB = x
A
B
0
1
00 01 11 10
x
A
Bx
X
1
X
X
X
1
KA = B∙x
A
B
0
1
00 01 11 10
x
A
Bx
X
1
X
X
X
KB = (A  x)'
A
B
0
1
00 01 11 10
x
A
Bx
X
1
X
1
X
X

## Slide 26: 6.4 Design: Example #1 (5/5)
Flip-flop input functions:
  JA = B∙x' JB = x
  KA = B∙x KB = (A  x)'
Logic diagram:
x
B
A
CP
J
Q
Q'
K
J
Q
Q'
K
With the flip-flop input functions,
we can derive the actual values for all the don’t-care terms and complete the truth table and state diagram.

## Slide 27: Q2 Circuit Design – JK Flip-Flops
Present State |  | Input | Next State |  | Flip-flop A |  | Flip-flop B | 
A | B | x | A+ | B+ | JA | KA | JB | KB
0 | 0 | 0 |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  | 

## Slide 28: Q2 Circuit Design – JK Flip-Flops
Present State |  | Input | Next State |  | Flip-flop A |  | Flip-flop B | 
A | B | x | A+ | B+ | JA | KA | JB | KB
0 | 0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 1 | 1 | 0 |  |  |  | 
0 | 1 | 0 | 1 | 0 |  |  |  | 
0 | 1 | 1 | 0 | 0 |  |  |  | 
1 | 0 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 1 | 0 | 1 |  |  |  | 
1 | 1 | 0 | d | d |  |  |  | 
1 | 1 | 1 | d | d |  |  |  | 

## Slide 29: Q2 Circuit Design – JK Flip-Flops
Present State |  | Input | Next State |  | Flip-flop A |  | Flip-flop B | 
A | B | x | A+ | B+ | JA | KA | JB | KB
0 | 0 | 0 | 0 | 1 | 0 | d |  | 
0 | 0 | 1 | 1 | 0 | 1 | d |  | 
0 | 1 | 0 | 1 | 0 | 1 | d |  | 
0 | 1 | 1 | 0 | 0 | 0 | d |  | 
1 | 0 | 0 | 0 | 0 | d | 1 |  | 
1 | 0 | 1 | 0 | 1 | d | 1 |  | 
1 | 1 | 0 | d | d | d | d |  | 
1 | 1 | 1 | d | d | d | d |  | 
JK Flip-flop's
excitation table.

## Slide 30: Q2 Circuit Design – JK Flip-Flops
Present State |  | Input | Next State |  | Flip-flop A |  | Flip-flop B | 
A | B | x | A+ | B+ | JA | KA | JB | KB
0 | 0 | 0 | 0 | 1 | 0 | d | 1 | d
0 | 0 | 1 | 1 | 0 | 1 | d | 0 | d
0 | 1 | 0 | 1 | 0 | 1 | d | d | 1
0 | 1 | 1 | 0 | 0 | 0 | d | d | 1
1 | 0 | 0 | 0 | 0 | d | 1 | 0 | d
1 | 0 | 1 | 0 | 1 | d | 1 | 1 | d
1 | 1 | 0 | d | d | d | d | d | d
1 | 1 | 1 | d | d | d | d | d | d
JK Flip-flop's
excitation table.

## Slide 31: Q2 Circuit Design – JK Flip-Flops
Present State |  | Input | Flip-flop A |  | Flip-flop B | 
A | B | x | JA | KA | JB | KB
0 | 0 | 0 | 0 | d | 1 | d
0 | 0 | 1 | 1 | d | 0 | d
0 | 1 | 0 | 1 | d | d | 1
0 | 1 | 1 | 0 | d | d | 1
1 | 0 | 0 | d | 1 | 0 | d
1 | 0 | 1 | d | 1 | 1 | d
1 | 1 | 0 | d | d | d | d
1 | 1 | 1 | d | d | d | d

## Slide 32: Q2 Circuit Design – JK Flip-Flops
JA = B∙x' + B'∙x = B ⊕ x
KA = 1
JB = A'∙x' + A∙x = A  x
KB = 1
Notes: Fewest logic gates

## Slide 33: Q2 Circuit Design – JK Flip-Flops
JA = B∙x' + B'∙x = B ⊕ x
KA = 1
JB = A'∙x' + A∙x = A  x
KB = 1

## Slide 34: Q2 Circuit Design – JK Flip-Flops
JA = B∙x' + B'∙x = B ⊕ x KA = 1
JB = A'∙x' + A∙x = A ʘ x KB = 1
Present State |  | Input | Next State |  | Flip-flop A |  | Flip-flop B | 
A | B | x | A+ | B+ | JA | KA | JB | KB
0 | 0 | 0 | 0 | 1 | 0 | d(1) | 1 | d(1)
0 | 0 | 1 | 1 | 0 | 1 | d(1) | 0 | d(1)
0 | 1 | 0 | 1 | 0 | 1 | d(1) | d(1) | 1
0 | 1 | 1 | 0 | 0 | 0 | d(1) | d(0) | 1
1 | 0 | 0 | 0 | 0 | d(0) | 1 | 0 | d(1)
1 | 0 | 1 | 0 | 1 | d(1) | 1 | 1 | d(1)
1 | 1 | 0 | d(0) | d(0) | d(1) | d(1) | d(0) | d(1)
1 | 1 | 1 | d(0) | d(0) | d(0) | d(1) | d(1) | d(1)

## Slide 35: Q2 Circuit Design – JK Flip-Flops
JA = B∙x' + B'∙x = B ⊕ x KA = 1
JB = A'∙x' + A∙x = A  x KB = 1
Present State |  | Input | Next State |  | Flip-flop A |  | Flip-flop B | 
A | B | x | A+ | B+ | JA | KA | JB | KB
0 | 0 | 0 | 0 | 1 | 0 | d(1) | 1 | d(1)
0 | 0 | 1 | 1 | 0 | 1 | d(1) | 0 | d(1)
0 | 1 | 0 | 1 | 0 | 1 | d(1) | d(1) | 1
0 | 1 | 1 | 0 | 0 | 0 | d(1) | d(0) | 1
1 | 0 | 0 | 0 | 0 | d(0) | 1 | 0 | d(1)
1 | 0 | 1 | 0 | 1 | d(1) | 1 | 1 | d(1)
1 | 1 | 0 | d(0) | d(0) | d(1) | d(1) | d(0) | d(1)
1 | 1 | 1 | d(0) | d(0) | d(0) | d(1) | d(1) | d(1)
A circuit is self-correcting if for some reason the circuit enters into any unused (invalid) state, it is able to transit to a valid state after a finite number of transitions.
Notes: State 3 always goes to state 0 which is a used state, regardless of input.

## Slide 36: Q3 Circuit Design – All Flip-Flops
A: D flip-flop,
B, C: T flip-flops,
D: JK flip-flop

## Slide 37: Q3 Circuit Design – All Flip-Flops
Current State |  |  |  | Next State |  |  |  |  |  |  | 
A | B | C | D | DA=A+ | B+ | C+ | D+ | TB | TC | JD | KD
0 | 0 | 0 | 0 | X | X | X | X | X | X | X | X
0 | 0 | 0 | 1 |  |  |  |  |  |  |  | 
0 | 0 | 1 | 0 |  |  |  |  |  |  |  | 
0 | 0 | 1 | 1 |  |  |  |  |  |  |  | 
0 | 1 | 0 | 0 |  |  |  |  |  |  |  | 
0 | 1 | 0 | 1 |  |  |  |  |  |  |  | 
0 | 1 | 1 | 0 |  |  |  |  |  |  |  | 
0 | 1 | 1 | 1 |  |  |  |  |  |  |  | 
1 | 0 | 0 | 0 | X | X | X | X | X | X | X | X
1 | 0 | 0 | 1 |  |  |  |  |  |  |  | 
1 | 0 | 1 | 0 | X | X | X | X | X | X | X | X
1 | 0 | 1 | 1 |  |  |  |  |  |  |  | 
1 | 1 | 0 | 0 | X | X | X | X | X | X | X | X
1 | 1 | 0 | 1 |  |  |  |  |  |  |  | 
1 | 1 | 1 | 0 | X | X | X | X | X | X | X | X
1 | 1 | 1 | 1 |  |  |  |  |  |  |  | 
Notes: We don’t care about state 0, and all even states after and including 8, i.e. 8, 10, 12 and 14

## Slide 38: Q3 Circuit Design – All Flip-Flops
Current State |  |  |  | Next State |  |  |  |  |  |  | 
A | B | C | D | DA=A+ | B+ | C+ | D+ | TB | TC | JD | KD
0 | 0 | 0 | 0 | X | X | X | X | X | X | X | X
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 |  |  |  | 
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 |  |  |  | 
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 |  |  |  | 
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 |  |  |  | 
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 |  |  |  | 
0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 |  |  |  | 
0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |  |  |  | 
1 | 0 | 0 | 0 | X | X | X | X | X | X | X | X
1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |  |  |  | 
1 | 0 | 1 | 0 | X | X | X | X | X | X | X | X
1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 |  |  |  | 
1 | 1 | 0 | 0 | X | X | X | X | X | X | X | X
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 |  |  |  | 
1 | 1 | 1 | 0 | X | X | X | X | X | X | X | X
1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 |  |  |  | 
Notes: State 1 goes to state 3

## Slide 39: Q3 Circuit Design – All Flip-Flops
Current State |  |  |  | Next State |  |  |  |  |  |  | 
A | B | C | D | DA=A+ | B+ | C+ | D+ | TB | TC | JD | KD
0 | 0 | 0 | 0 | X | X | X | X | X | X | X | X
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | X | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | X
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | X | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | X
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | X | 0
0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | X
0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | X | 0
1 | 0 | 0 | 0 | X | X | X | X | X | X | X | X
1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | X | 0
1 | 0 | 1 | 0 | X | X | X | X | X | X | X | X
1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | X | 0
1 | 1 | 0 | 0 | X | X | X | X | X | X | X | X
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | X | 0
1 | 1 | 1 | 0 | X | X | X | X | X | X | X | X
1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | X | 1
JK Flip-flop
D Flip-flop
T Flip-flop

## Slide 40: Q3 Circuit Design – All Flip-Flops
DA = A∙B' + A∙C' + A'∙B∙C∙D
TB = C
TC = A' + B' + C'
JD = B∙C
KD = A∙B∙C

## Slide 41: Q3 Circuit Design – All Flip-Flops
Current State |  |  |  | Next State |  |  |  |  |  |  | 
A | B | C | D | DA=A+ | B+ | C+ | D+ | TB | TC | JD | KD
0 | 0 | 0 | 0 | X(0) | X | X | X | X(0) | X(1) | X(0) | X(0)
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | X | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | X
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | X | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | X
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | X | 0
0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | X
0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | X | 0
1 | 0 | 0 | 0 | X(1) | X | X | X | X(0) | X(1) | X(0) | X(0)
1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | X | 0
1 | 0 | 1 | 0 | X(1) | X | X | X | X(1) | X(1) | X(0) | X(0)
1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | X | 0
1 | 1 | 0 | 0 | X(1) | X | X | X | X(0) | X(1) | X(0) | X(0)
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | X | 0
1 | 1 | 1 | 0 | X(0) | X | X | X | X(1) | X(0) | X(1) | X(1)
1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | X | 1
DA = A∙B' + A∙C' + A'∙B∙C∙D
TB = C
TC = A' + B' + C'
JD = B∙C
KD = A∙B∙C
Notes: With the expressions, we can fill up DA, TB, TC, JD and KD.
Alternatively, we can also look at the X used in each K-map, each X used indicates an 1, otherwise it is a 0. E.g. in TC, ABCD = 0000, 1000, 1010 and 1100 are used, 1110 is ununsed.

## Slide 42: Q3 Circuit Design – All Flip-Flops
Current State |  |  |  | Next State |  |  |  |  |  |  | 
A | B | C | D | DA=A+ | B+ | C+ | D+ | TB | TC | JD | KD
0 | 0 | 0 | 0 | X(0) | X(0) | X(1) | X(0) | X(0) | X(1) | X(0) | X(0)
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | X | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | X
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | X | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | X
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | X | 0
0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | X
0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | X | 0
1 | 0 | 0 | 0 | X(1) | X(0) | X(1) | X(0) | X(0) | X(1) | X(0) | X(0)
1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | X | 0
1 | 0 | 1 | 0 | X(1) | X(1) | X(0) | X(0) | X(1) | X(1) | X(0) | X(0)
1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | X | 0
1 | 1 | 0 | 0 | X(1) | X(1) | X(1) | X(0) | X(0) | X(1) | X(0) | X(0)
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | X | 0
1 | 1 | 1 | 0 | X(0) | X(0) | X(1) | X(1) | X(1) | X(0) | X(1) | X(1)
1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | X | 1
 = clock transition LOW to HIGH
Notes: Based on the values, we can also fill up on A+, B+, C+ and D+

## Slide 43: Q3 Circuit Design – All Flip-Flops
Current State |  |  |  | Next State |  |  | 
A | B | C | D | DA=A+ | B+ | C+ | D+
0 | 0 | 0 | 0 | X(0) | X(0) | X(1) | X(0)
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | X(1) | X(0) | X(1) | X(0)
1 | 0 | 0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 1 | 0 | X(1) | X(1) | X(0) | X(0)
1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 0 | X(1) | X(1) | X(1) | X(0)
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | X(0) | X(0) | X(1) | X(1)
1 | 1 | 1 | 1 | 0 | 0 | 1 | 0
Self-correcting!

## Slide 44
Q4(a).
00
01
10
11
00
00
00
10
The circuit consists of 4 states representing the amount a visitor has deposited.
Two types of token: Pokemoney $1 (P$1) and Pokemoney $2 (P$2).
The visitor can deposit only one token at a time.
The circuit remains at state 3 when the token value exceeds 3.
The inputs x and y represent the P$1 and P$2 tokens respectively. The label on each arrow represents xy.
The left bit represents if $1 is deposited.
The right bit represents if $2 is deposited.

## Slide 45
Q4(a).
00,01,10
01
01
10
10,01
00
01
10
11
00
00
00
10
The circuit consists of 4 states representing the amount a visitor has deposited.
Two types of token: Pokemoney $1 (P$1) and Pokemoney $2 (P$2).
The visitor can deposit only one token at a time.
The circuit remains at state 3 when the token value exceeds 3.
The inputs x and y represent the P$1 and P$2 tokens respectively. The label on each arrow represents xy.
The left bit represents if $1 is deposited.
The right bit represents if $2 is deposited.
Notes: The left bit represents if $1 is deposited. The right bit represents if $2 is deposited.

## Slide 46
Q4(b).
Present | B | Inputs | y | Next | B+
A | B | x | y | A+ | B+
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | X | X
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | X | X
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | X | X
1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | X | X
A
0
1
X
0
0
1
X
1
1
1
X
1
1
1
1
X
B
x
y
DA = A+
A
0
0
X
1
1
1
X
0
1
1
X
1
1
0
1
X
B
x
y
DB = B+
DA = A + y + Bx
DB = Bx' + B'x + Ay + Ax
or DB = Bx' + B'x + Ay + AB
00
01
10
11
00
00
00
00,01,10
01
01
10
10,01
10

## Slide 47
Circuit
Obtain flip-flop inputs and circuit output (if any) expressed with the present state and input (if any).
Draw truth table.
Fill up the present state, input (if any), output (if any) and flip-flop inputs.
State Diagram
Obtain the next state using characteristic table.
Sequential Circuit Analysis
Circuit
Obtain flip-flop inputs from excitation table.
Get simplified expression for flip-flop inputs using K-maps.
Draw truth table.
Fill up the present state, input (if any), output (if any), the next state
State Diagram
Fill up flip-flop inputs for unused states.
Obtain the next state for unused states using characteristic table.
Sequential Circuit Design

## Slide 48
Final Exam Instructions
Notes: I am allowed to show you the final exam instructions.
Final is not far
Read carefully and let me know if you spot any ambiguities

## Slide 49: CS2100 Tutorial 9
Song Kai
song.kai@nus.edu.sg