## Slide 1: CS2100 Tutorial 11
Song Kai
song.kai@nus.edu.sg
Student Feedback Portal

## Slide 2: 1. Memory Hierarchy
Size
SRAM
DRAM
Harddisk
Speed
Registers
Memory
(DRAM)
Devices
Input
Output
Processor
Control
Datapath
Registers
Cache
(SRAM)
Notes: Smaller the size, faster the speed
Static RAM
Dynamic RAM
To bridge the gap

## Slide 3: 2.2 Memory Access Time: Terminology
Memory
Processor
Cache
X
Y
Hit: Data is in cache (e.g., X)
  Hit rate: Fraction of memory accesses that hit
  Hit time: Time to access cache
Miss: Data is not in cache (e.g., Y)
  Miss rate = 1 – Hit rate
  Miss penalty: Time to replace cache block + hit time
Hit time << Miss penalty

## Slide 4: 2.2 Memory Access Time: Formula
Average Access Time
= Hit rate x Hit Time + (1-Hit rate) x Miss penalty
Example:
Suppose our on-chip SRAM (cache) has 0.8 ns access time, but the fastest DRAM (main memory) we can get has an access time of 10ns. How high a hit rate do we need to sustain an average access time of 1ns?

Let h be the desired hit rate.
1 = 0.8h + (1 – h)  (10 + 0.8) = 0.8h + 10.8 – 10.8h
10h = 9.8  h = 0.98
Hence we need a hit rate of 98%.
  Time to replace cache block + hit time

## Slide 5: 6. Types of Cache Misses
Compulsory misses
  On the first access to a block; the block must be brought into the cache
  Also called cold start misses or first reference misses
Conflict misses
  Occur in the case of direct mapped cache or set associative cache, when several blocks are mapped to the same cache block/set
  Also called collision misses or interference misses
Capacity misses
  Occur when blocks are discarded from cache as cache cannot contain all blocks needed (fully associative cache)

## Slide 6: Direct Mapped Cache
Given a cache of size 2i+b bytes, we divide it into 2i blocks, each block contains 2b bytes.
Given a memory of size 2m bytes, we place each block of memory into a block in cache.
i+b-1
Memory Address
m
0
b-1
b
Tag
Offset
Index
Direct
Mapped Cache
00
01
10
11
Index
Data
Tag
Valid
2b bytes data contained in these 2b memory addresses
Cache size: 16KB
Block size: 16 bytes, b = 4
# blocks = 1024, i = 10
Memory: 1GB
m = 30
Tag = m – i – b = 16 bits
Notes: Assuming byte addressable.
We put a block of data with the same tag and index into a block of cache.
For memory addresses with the same index will all be placed in the same block in cache.
Valid and tag do not count into the cache size

## Slide 7: 4. Cache Circuitry: Example
10
Index
18
Tag
Hit
Data
32
16-KB cache:
4-word (16-byte) blocks
1024 blocks
31 30 . . . 15 14 13 . . . 5 4 3 2 1 0
Tag
Index
Ofst
0
1
2
.
.
.
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Cache Hit =
[Tag Matches] AND [Valid]
18
MUX
Block offset
2 (Addr[3:2])
Notes: We store a block but only take out a word each time

## Slide 8: 5. Reading Data: Initial State
Intially cache is empty
   All valid bits are zeroes (false)
0
0
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index

## Slide 9: 5. Reading Data: Load #1-1
0
0
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Load from
Step 1. Check Cache Block at index 1
000000000000000000
0100
Tag
Offset
0000000001
Index

## Slide 10: 5. Reading Data: Load #1-2
Load from
Step 2. Data in block 1 is invalid [Cold/Compulsory Miss]
000000000000000000
0100
Tag
Offset
0000000001
Index
0
0
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index

## Slide 11: 5. Reading Data: Load #1-3
Load from
Step 3. Load 16 bytes from memory; Set Tag and Valid bit
000000000000000000
0100
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Notes: How do we decide the data to be placed?
Offset  word 0 contains bytes 0 -3, corresponding to offset 0000 - 0011

## Slide 12: 5. Reading Data: Summary
Read address (RA) sent from processor  cache
In cache?
Access memory block at RA
Use Offset and delivery data to processor
Load into cache line
Set Tag and Valid bit (if needed)
Allocate cache line
Read Hit
[Tags Match] AND [Valid]
Read Miss
[Tags Mismatch] OR [!Valid]

## Slide 13: 8. Changing Cache Content: Write Policy
Cache and main memory are inconsistent
  Modified data only in cache, not in memory!
Solution 1: Write-through cache
  Write data both to cache and to main memory
Solution 2: Write-back cache
  Only write to cache
  Write to main memory only when cache block is replaced (evicted)
On a Cache Hit!

## Slide 14: 8. Write-Through Cache
Problem:
  Write will operate at the speed of main memory!
Solution:
  Put a write buffer between cache and main memory
    Processor: writes data to cache + write buffer
    Memory controller: write contents of the buffer to memory
Processor
Cache
Write Buffer
DRAM

## Slide 15: 8. Write-Back Cache
Problem:
  Quite wasteful if we write back every evicted cache blocks
Solution:
  Add an additional bit (Dirty bit) to each cache block
  Write operation will change dirty bit to 1
    Only cache block is updated, no write to memory
  When a cache block is replaced:
    Only write back to memory if dirty bit is 1

## Slide 16: 8. Handling Cache Misses
On a Read Miss:
  Data loaded into cache and then load from there to register
Write Miss option 1: Write allocate
  Load the complete block into cache
  Change only the required word in cache
  Write to main memory depends on write policy
Write Miss option 2: Write around
  Do not load the block to cache
  Write directly to main memory only

## Slide 17: 8. Writing Data: Summary
Write address (WA) and value sent from processor  cache
In cache?
Depends on
Write Miss Policy
(Write Allocate) or (Write Around)
Depends on
Write Policy
(Write Back)
or (Write Through)
Write Hit
[Tags Match] AND [Valid]
Write Miss
[Tags Mismatch] OR [!Valid]

## Slide 18: Q1 Direct-Mapped Cache 16 1-Word Blocks
MIPS machine  4 bytes per word, 32-bit address
Each block contains 4 bytes  Len(Offset) = 2 bits
16 cache blocks  Len(Index) = 4 bits
Len(Tag) = 32 – 2 – 4 = 26 bits
Does not matter that much
4: 00…00 0001 00
16: 00…00 0100 00
32: 00…00 1000 00
20: 00…00 0101 00
80: 00…01 0100 00
68: 00…01 0001 00
76: 00…01 0011 00
224: 00…11 1000 00
36: 00…00 1001 00
44: 00…00 1011 00
16: 00…00 0100 00
172: 00…10 1011 00
20: 00…00 0101 00
24: 00…00 0110 00
36: 00…00 1001 00
68: 00…01 0001 00
i+b-1
Memory Address
m
0
b-1
b
Tag
Offset
Index

## Slide 19
4: 00…00 0001 00
16: 00…00 0100 00
32: 00…00 1000 00
20: 00…00 0101 00
80: 00…01 0100 00
68: 00…01 0001 00
76: 00…01 0011 00
224: 00…11 1000 00
36: 00…00 1001 00
44: 00…00 1011 00
16: 00…00 0100 00
172: 00…10 1011 00
20: 00…00 0101 00
24: 00…00 0110 00
36: 00…00 1001 00
68: 00…01 0001 00
Index | Valid | Tag | Word
0 | 0 |  | 
1 | 0 |  | 
2 | 0 |  | 
3 | 0 |  | 
4 | 0 |  | 
5 | 0 |  | 
6 | 0 |  | 
7 | 0 |  | 
Index | Valid | Tag | Word
8 | 0 |  | 
9 | 0 |  | 
10 | 0 |  | 
11 | 0 |  | 
12 | 0 |  | 
13 | 0 |  | 
14 | 0 |  | 
15 | 0 |  | 
M[4]
1
0
M[16]
1
0
M[32]
1
0
M[20]
1
0
M[80]
1
M[68]
1
M[76]
1
1
M[224]
3
M[36]
1
0
M[44]
1
0
M[16]
0
M[172]
2
Hit
M[24]
1
0
Hit
Hit
Offset = 2 bits, Index = 4 bits, Tag = 26 bits
Q1 Direct-Mapped Cache
16 1-Word Blocks

## Slide 20: 3. Set Associative (SA) Cache
N-way Set Associative Cache
  Cache consists of a number of sets:
    Each set contains N cache blocks
  Each memory block maps to a unique cache set
  Within the set, a memory block can be placed in any of the N cache blocks in the set
2-way Set Associative Cache
00
01
10
11
Set Index
Data
Tag
Valid
Data
Tag
Valid
Set
Notes: The two blocks together forms a set, they have the same set index
If one block in the set is filled, we will put the data into another block

## Slide 21: Set Associative Cache
Given a 2n-way set associative cache of size 2s+n+b bytes,
we divide it into 2s sets, each set contains 2n blocks. Each block contains 2b bytes.
Given a memory of 2m bytes, we place each block of memory into a block in a set of the cache.
s+b-1
Memory Address
m
0
b-1
b
Tag
Offset
Set Index
16KB 4-way cache
Block size: 8 bytes, b = 3
Set size: 8 x 4 = 32 bytes
#sets = 16KB / 32 bytes = 512,
s = 9
Memory: 2GB
m = 31
Tag = m – s – b = 19 bits
2-way Set Associative Cache
00
01
10
11
Set Index
Data
Tag
Valid
Data
Tag
Valid
Set

## Slide 22: 3. Set Associative Cache: Circuitry
Hit
Data
0
1
2
.
.
.
254
255
V
Tag
Data
0
1
2
.
.
.
254
255
V
Tag
Data
0
1
2
.
.
.
254
255
V
Tag
Data
0
1
2
.
.
.
254
255
V
Tag
Data
22
=
=
=
22
22
22
A
=
B
C
D
31 30 . . . 11 10 9 . . . 2 1 0
Tag
Idx
Ofst
4 x 1 Select
A
B
C
D
8
Set Index
22
Tag
32
4-way 4-KB cache: 1-word (4-byte) blocks
Note the simultaneous "search" on all tags of a set.
set size = 4 byte x 4 = 16 bytes
#sets = 4KB / 16 bytes = 256
b = 2, s = 8,
Len(tag) = Len(addr) – 2 – 8

## Slide 23: 5. Block Replacement Policy (1/3)
Set Associative or Fully Associative Cache:
  Can choose where to place a memory block
  Potentially replacing another cache block if full
  Need block replacement policy
Least Recently Used (LRU)
  How: For cache hit, record the cache block that was accessed
    When replacing a block, choose one which has not been accessed for the longest time
  Why: Temporal locality
Notes: for direct mapped cache, we always replace the old with the new. No policy is needed

## Slide 24: 5. Block Replacement Policy (2/3)
Least Recently Used policy in action:
  4-way SA cache
  Memory accesses: 0 4 8 12 4 16 12 0 4
8
12
4
16
4
16
12
0
0
4
8
12
LRU
0
8
12
4
8
4
16
12
16
12
0
4
Hit
Miss (Evict Block 0)
Hit
Miss (Evict Block 8)
Hit
Access 4
Access 16
Access 12
Access 0
Access 4
x
x
Notes: The illustration here refer to a set. Each set contains 4 blocks.
We always move the newly accessed block to the right, so that the left-most block contains the LRU and will be evicted
This is an illustration of the data structure to do replacement. The data in cache is not shifted

## Slide 25: 5. Block Replacement Policy (3/3)
Drawback for LRU
  Hard to keep track if there are many choices
Other replacement policies:
  First in first out (FIFO)
  Random replacement (RR)
  Least frequently used (LFU)

## Slide 26: Q2 2-Way Set Associative Cache 16 words, 2-word blocks
MIPS machine  4 bytes per word, 32-bit memory address
Cache size: 4 bytes x 16 = 64 bytes
2-word Blocks  8-byte per block  Len(Offset) = 3 bits
set size = 2 x 8 byte = 16 bytes
#sets = 64 bytes / 16 bytes = 4  Len(Set Index) = 2 bits
Len(Tag) = m – s – b = 32 – 5 = 27 bits
4: 00…000 00 100
16: 00…000 10 000
32: 00…001 00 000
20: 00…000 10 100
80: 00…010 10 000
68: 00…010 00 100
76: 00…010 01 100
224: 00…111 00 000
36: 00…001 00 100
44: 00…001 01 100
16: 00…000 10 000
172: 00…101 01 100
20: 00…000 10 100
24: 00…000 11 000
36: 00…001 00 100
68: 00…010 00 100
s+b-1
Memory Address
m
0
b-1
b
Tag
Offset
Set Index

## Slide 27
4: 00…000 00 100
16: 00…000 10 000
32: 00…001 00 000
20: 00…000 10 100
80: 00…010 10 000
68: 00…010 00 100
76: 00…010 01 100
224: 00…111 00 000
36: 00…001 00 100
44: 00…001 01 100
16: 00…000 10 000
172: 00…101 01 100
20: 00…000 10 100
24: 00…000 11 000
36: 00…001 00 100
68: 00…010 00 100
Set | Valid | Tag | Word0 | Word1 | Valid | Tag | Word0 | Word1
0 | 0 |  |  |  | 0 |  |  | 
1 | 0 |  |  |  | 0 |  |  | 
2 | 0 |  |  |  | 0 |  |  | 
3 | 0 |  |  |  | 0 |  |  | 
4
M[0]
1
0
M[4]
M[16]
1
0
M[20]
M[32]
1
1
M[36]
Hit
M[80]
1
2
M[84]
M[64]
2
M[68]
M[72]
1
2
M[76]
M[224]
7
M[228]
M[32]
1
M[36]
M[40]
1
1
M[44]
Hit
M[168]
5
M[172]
Hit
M[24]
1
0
M[28]
Hit
M[64]
2
M[68]
Q2 2-Way Set Associative Cache
16 words, 2-word blocks
Offset = 3 bits, Index = 2 bits, Tag = m - 5 bits
Replacement Policy: LRU

## Slide 28: 4. Fully Associative (FA) Cache
Fully Associative Cache
  A memory block can be placed in any location in the cache
Key Idea:
  Memory block placement is no longer restricted by cache index or cache set index
  ++ Can be placed in any location, BUT
  --- Need to search all cache blocks for memory access
Notes: Only for very small caches, usually 8 or 16 blocks

## Slide 29: Fully Associative Cache
Given a fully associative cache of size 2i+b bytes,
we divide it into 2i blocks. Each block contains 2b bytes.
Given a memory of 2m bytes, we place each block of memory into a block in the cache.
16KB fully associative cache
Block size: 8 bytes, b = 3
Memory: 4GB
m = 32
Tag = m – b = 29 bits
m
0
b-1
Tag
Offset
b

## Slide 30: 4. Fully Associative Cache: Circuitry
Example:
  4KB cache size and 16-Byte block size
  Compare tags and valid bit in parallel
No Conflict Miss (since data can go anywhere)
... ... ... … … … … …
0
1
2
3
254
255
Index
Valid
Tag
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
m-bit
4-bit
Tag
Offset
=
=
=
=
=
=
b = 4
Tag = m – 4

## Slide 31
Q3.
# | Code
i0 i1 | [some instruction] addi $s0, $zero, 0
i2 | addi $s1, $s5, -1
i3 | addi $s3, $zero, 1
i4 | loop: slt $t0, $s0, $s1
i5 | beq $t0 $zero, exit
i6 | beq $s3, $zero, exit
i7 | addi $t1, $s4, $s0
i8 | lb $t4, 0($t3)
i9 | addi $t3, $s4, $s1
i10 | lb $t4, 0($t3)
i11 | beq $t2, $t4, else
i12 | addi $s3, $zero, 0
i13 | j endW
i14 | else: addi $s0, $s0, 1
i15 | addi $s1, $s1, -1
i16 | endW: j loop
i17 | exit: [some instruction]
Trace the first 10 iterations of the code
First iteration:
i1 – i11, (skip i12 – i13), i14 – i16
Subsequent iterations:
i4 – i11, (skip i12 – i13), i14 – i16
Assuming the string is a palindrome,
and sufficiently long
$s0 = 0
$s1 = size - 1
$s3 = 1
exit if $s0 = $s1
exit if unmatched
get low byte
get high byte
always go to else
update low & high
Notes: Recall that we have instruction memory and data memory. We also have instruction cache and data cache.

## Slide 32
Q3.
First iteration: i1 – i11, i14 – i16
Subsequent iterations: i4 – i11, i14 – i16
Direct mapped cache: 2 blocks, each 16 bytes
Show instruction cache content at end of 1st iteration
Calculate total cache hits after 10 iterations
Cache block 0 |  |  |  | 
Cache block 1 |  |  |  | 
inst | H/M?
i1
M
i0
i1
i2
i3
i4
i5
i6
i7
i8
i9
i10
i11
i12
i13
i14
i15
i16
i17
i18
i19
i2
H
i3
H
i4
M
i5
H
i6
H
i7
H
i8
M
i9
H
i10
H
i11
H
i14
M
i15
H
i16
M
First iteration:
Subsequent iterations
First iteration: 9 hits
Each of next 9 iterations: 7 hits
Total hits = 9 + (7 × 9) = 72
16-byte Block  Offset = 4 bits
2 Blocks  Index = 1 bit
i0: 00…000 0 0000
i1: 00…000 0 0100
i2: 00…000 0 1000
i3: 00…000 0 1100
i4: 00…000 1 0000
i8: 00…001 0 0000
i14: 00…001 1 1000
I16: 00…010 0 0000

## Slide 33
Q3.
First iteration: i1 – i11, i14 – i16
Subsequent iteration: i4 – i11, i14 – i16
Direct mapped cache: 4 blocks, each 8 bytes
Show instruction cache content at end of 1st iteration
Calculate total cache hits after 10 iterations
Cache block 0 |  | 
Cache block 1 |  | 
Cache block 2 |  | 
Cache block 3 |  | 
inst | H/M?
i1
M
i0
i1
i2
i3
i4
i5
i6
i7
i8
i9
i10
i11
i16
i17
i14
i15
i16
i17
i14
i15
i2
M
i3
H
i4
M
i5
H
i6
M
i7
H
i8
M
i9
H
i10
M
i11
H
i14
M
i15
H
i16
M
First iteration:
inst | H/M?
Subsequent iterations:
i4
i5
i6
i7
i8
i9
i10
i11
i14
i15
i16
H
H
M
H
M
H
H
H
M
H
M
i6
i7
i8
i9
First iteration: 6 hits
Each of next 9 iterations: 7 hits
Total hits = 6 + (7 × 9) = 69
8-byte Block  Offset = 3 bits
4 Blocks  Index = 2 bit
i0: 00…000 00 000
i1: 00…000 00 100
i2: 00…000 01 000
i3: 00…000 01 100
i4: 00…000 10 000
i8: 00…001 00 000
i14: 00…001 11 000
i16: 00…010 00 000

## Slide 34
Q3.
Direct mapped cache: 2 blocks, each 8 bytes
String is 64-character long and is a palindrome; first character at 0x1000
Final content of data cache
Hit rate
Cache block 0 | 
Cache block 1 | 
For each block, first character is a miss, the remaining 7 characters accessed are hits.
Total % hits = 7/8= 87.5%
s[0]
s[63]
…
R
E
A
D
Y
Y
D
A
E
R
s[62]
s[1]
s[2]
s[61]
Access pattern: s[0], s[63], s[1], s[62], …, s[31], s[32]
char | H/M?
s[0]
M
s[0..7]
s[63]
M
Addr 0x1000  block 0
Addr 0x103F  block 1
s[56..63]
1 bit
3 bits
tag
index
offset
s[1]
H
s[62]
H
:
s[8..15]
s[48..55]
s[16..23]
s[40..47]
s[24..31]
s[32..39]
s[8]
M
s[55]
M
:
s[0..7]
s[8..15]
s[16..23]
s[24..31]
s[32..39]
s[40..47]
s[48..55]
s[56..63]
0000 0000 0000 0000 0001 0000 0000 0000
Addr 0x1008  block 1
Addr 0x1037  block 0

## Slide 35
Q3.
Direct mapped cache: 2 blocks, each 8 bytes
String is 72-character long and is a palindrome; first character at 0x1000
Hit rate
Cache block 0 | 
Cache block 1 | 
Only 7 hits in the last examined block s[32..39]  7/72 = 9.72%
s[0]
s[71]
…
R
E
A
D
Y
Y
D
A
E
R
s[70]
s[1]
s[2]
s[69]
Access pattern: s[0], s[71], s[1], s[70], …, s[35], s[36]
char | H/M?
s[0]
M
s[0..7]
s[71]
M
Addr 0x1000  block 0
Addr 0x1047  block 0!
s[8..15]
1 bit
3 bits
tag
index
offset
s[1]
M
s[70]
M
:
s[8]
M
s[63]
M
:
s[64..71]
s[0..7]
s[64..71]
Addr 0x1008  block 1
Addr 0x103F  block 1!
s[56..63]
s[9]
M
s[8..15]
s[62]
M
s[56..63]
Data that go into cache block 0: s[0..7], s[64..71], s[16..23], s[48..55], s[32..39]
Data that go into cache block 1: s[8..15], s[56..63], s[24..31], s[40..47]
This is known as cache thrashing.
s[0..7]
s[8..15]
s[16..23]
s[24..31]
s[32..39]
s[40..47]
s[48..55]
s[56..63]
s[64..71]

## Slide 36
Final
Cache
Pipelining
Sequential Circuits
MSI Components
Combinational Circuits
Boolean Algebra, Simplification
Midterm
MIPS Datapath and Control
MIPS Instruction Encoding
MIPS Syntax
Pointers, Arrays, Strings, Structs
Number Systems
C Programming
It is a pleasure meeting all of you, my friends.

## Slide 37: CS2100 Tutorial 11
Song Kai
song.kai@nus.edu.sg
Student Feedback Portal
Credit to Mr Tan Yi Qian